## Slide 1: IETF 95 – Buenos Aires April 2016
YANG Data Model for
LDP and mLDP
(draft-raza-mpls-ldp-mldp-yang-03)
            Kamran Raza (Cisco)
            Rajiv Asati (Cisco)
            Reshad Rahman (Cisco)
            Santosh Esale (Juniper)
            Xufeng Liu (Ericsson)
            Jeff Tantsura (Ericsson)
            Xia Chen (Huawei)
            Loa Andresson (Huawei)
            Himanshu Shah (Ciena)
            Matthew Bocci (Alcatel-Lucent)
            … and several other contributors as acknowledged in the draft

## Slide 2: Changes in Rev -03
Addressed comments from MPLS WG chair (Ross Callon)
Added high-level LDP YANG tree illustration
Defined and clarified the use of terms LDP Neighbor/Adjacency, Session, Peer
  Makes changes in the document to adhere to above defs.
Added Derived/Operational state for LDP
Re-organized and Cleaned up the doc for clarity
Limited number of authors to 6 on the main page
Notes: Changes LSR-ID from union type to leaf (yang:dotted-quad) was done in version -02.

## Slide 3: Ross Callon’s Comments
Boiler plate rfc2119
Update “Security Consideration” section
Clarify IANA section
Normative references
Number of authors
IDNITs

## Slide 4: High-level LDP YANG tree
Better illustration in -03:

## Slide 5: LDP Neighbor/Adjacency, Session and Peer
Our model uses the terms LDP neighbor/adjacency, session, and peer more strictly than RFC 5036 does.
In this model, these terms are meant as follows:
  Neighbor/Adjacency: An LDP enabled LSR that is discovered through LDP (basic/extended) discovery mechanisms.
  Session: An LDP neighbor with whom a TCP connection has been established
  Peer: An LDP session which has successfully progressed beyond its initialization phase and is ready for binding exchange.
When used in our model, the above terms refer strictly to the semantics and definitions defined for them.

## Slide 6: Derived State: LDP
LDP operational/derived state is defined for 4 areas:
  Neighbor Adjacencies
  Peer
  Bindings:
    Address
    FEC-label
  Capabilities
  Note that “applied” state is not presented here as it has been covered as part of intended (configuration) state.
Note: See additional slides section for complete “derived state” yang tree

## Slide 7: Cross-WG Item Closure
LSR-Id
  dotted-quad vs uint32 vs ip-address !!
  Consistency with other routing protocol router-id

## Slide 8: TO-DO List/Items
Complete Operational/state model for mLDP
Ensure Alignment with mpls-base
Ensure Alignment with netmod WG direction
  Ensure Alignment with routing module changes : network-instance vs routing-instance.

## Slide 9: Next Steps
Request WG adoption
Close/Keep up with the TODO list (ongoing)
  Will continue even after the WG adoption

## Slide 10: Backup Slide

## Slide 11: LDP: Config Hierarchy
module: ietf-mpls-ldp
+-- routing
+-- routing-instance [name]
+-- mpls
+-- mpls-ldp
+-- global
| +-- ...
| +-- ...
| +-- address-family* [afi]
| +-- . . .
| +-- . . .
| +-- discovery
| +-- . . .
+-- peers
+-- ...
+-- …

## Slide 12: Derived State: LDP Nbr/Adj (1)
Firstly, High level organization of the Nbr/Adj state:
+--rw mpls-ldp!
+--rw discovery
+--rw interfaces
| +--rw interface* [interface]
| +--rw address-family* [af]
| +--ro state
| +--ro ipv4 (or ipv6)
| +--ro hello-adjacencies* [adjacent-address]
| +--ro adjacent-address
| . . . .
| . . . .
+--rw targeted
+--rw address-family* [afi]
+--rw afi address-family
+--ro state
+--ro ipv4 (or ipv6)
+--ro hello-adjacencies* [local-address adjacent-address]
+--ro local-address
+--ro adjacent-address
. . . .
. . . .

## Slide 13: Derived State: LDP Nbr/Adj (2)
Following are nbr/adj state attributes:
+--ro hello-adjacencies* [adjacent-address]
+--ro adjacent-address inet:ipv4-address
+--ro flag* identityref
+--ro hello-holdtime
+--ro adjacent? Uint16
+--ro negotiated? Uint16
+--ro remaining? Uint16
+--ro next-hello? Uint16
+--ro statistics
+--ro discontinuity-time yang:date-and-time
+--ro hello-received? yang:counter64
+--ro hello-dropped? yang:counter64
+--ro peer? Leafref

## Slide 14: Derived State: LDP Peer (1)
Firstly, High level organization of the peer state:
+--rw mpls-ldp!
+--rw peers
+--rw peer* [lsr-id]
+--rw lsr-id
+--ro state
+-- . . . .
+-- . . . .
+--ro capability
| +--. . . .
+--ro address-family
| +--ro ipv4 (or ipv6)
| +--ro hello-adjacencies* [local-address adjacent-address]
| +-- . . . .
+--ro received-peer-state
| +-- . . . .
| +--ro capability
| . . . .
+--ro statistics
+-- . . . .
+-- . . . .

## Slide 15: Derived State: LDP Peer (2)
Following are peer state attributes:
+--rw peers
+--rw peer* [lsr-id]
+--rw lsr-id yang:dotted-quad
+--ro state
+--ro label-advertisement-mode
| +--ro local? label-adv-mode
| +--ro peer? label-adv-mode
| +--ro negotiated? label-adv-mode
+--ro next-keep-alive? uint16
+--ro peer-ldp-id? yang:dotted-quad
+--ro received-peer-state
| +--ro graceful-restart
| | +--ro enable? boolean
| | +--ro reconnect-time? uint16
| | +--ro recovery-time? uint16
| +--ro capability
| +--ro end-of-lib
| +--ro typed-wildcard-fec
| +--ro upstream-label-assignment

## Slide 16: Derived State: LDP Peer (3)
>> CONT’D
+--ro session-holdtime
| +--ro peer? uint16
| +--ro negotiated? uint16
| +--ro remaining? uint16
+--ro session-state? enumeration
+--ro tcp-connection
| +--ro local-address? inet:ip-address
| +--ro local-port? uint16
| +--ro remote-address? inet:ip-address
| +--ro remote-port? uint16
+--ro up-time? String

## Slide 17: Derived State: LDP Peer (4)
>> CONT’D
+--ro statistics
+--ro discontinuity-time yang:date-and-time
+--ro sent (and received)
| +--ro total-octets? yang:counter64
| +--ro total-messages? yang:counter64
| +--ro address? yang:counter64
| +--ro address-withdraw? yang:counter64
| +--ro initialization? yang:counter64
| +--ro keepalive? yang:counter64
| +--ro label-abort-request? yang:counter64
| +--ro label-mapping? yang:counter64
| +--ro label-release? yang:counter64
| +--ro label-request? yang:counter64
| +--ro label-withdraw? yang:counter64
| +--ro notification? yang:counter64
+--ro total-addresses? uint32
+--ro total-labels? uint32
+--ro total-fec-label-bindings? uint32

## Slide 18: Derived State: LDP Bindings (1)
Firstly, High level organization of the binding state:
+--rw mpls-ldp!
+--rw global
+--rw address-family* [afi]
+--rw afi address-family
+--ro state
+--ro ipv4 (or ipv6)
+--ro bindings
+--ro address* [address]
| +--ro address
| +--ro direction? advertised-received
| +--ro peer? leafref
+--ro fec-label* [fec]
+--ro fec inet:ipv4-prefix
+--ro peer* [direction peer]
+--ro direction advertised-received
+--ro peer leafref
+--ro label? uint32
+--ro used-in-forwarding? Boolean

## Slide 19: Derived State: LDP Bindings (2)
Example of address binding derived state:
Address bindings:
Addr 1.1.1.1:
advertised
Addr 1.1.1.2:
advertised
Addr 2.2.2.2:
received, peer 192.168.0.2
Addr 2.2.2.22:
received, peer 192.168.0.2
Addr 3.3.3.3:
received, peer 192.168.0.3
Addr 3.3.3.33:
received, peer 192.168.0.3

## Slide 20: Derived State: LDP Bindings (3)
Example of FEC-label binding derived state:
FEC-Label bindings:
FEC 200.1.1.1/32:
advertised: local-label 16000
peer 192.168.0.2:0
peer 192.168.0.3:0
peer 192.168.0.4:0
received:
peer 192.168.0.2:0, label 16002, used-in-forwarding=Yes
peer 192.168.0.3:0, label 17002, used-in-forwarding=No
FEC 200.1.1.2/32:
. . . .
FEC 201.1.0.0/16:
. . . .

## Slide 21: Derived State: LDP Capabilities
LDP capabilities state comprise two types of information:
  Global information (such as timer etc)
  Per-peer information.
+--rw mpls-ldp!
+--rw global
| +--ro state
| +--ro capability
| +--ro . . . .
| +--ro . . . .
+--rw peers
+--rw peer* [lsr-id]
+--rw lsr-id yang:dotted-quad
+--ro state
+--ro received-peer-state
+--ro capability
+--ro . . . .
+--ro . . . .