## Slide 1: Yang Model for PCEP
draft-pkd-pce-pcep-yang-05
Dhruv Dhody | Huawei
Jonathan Hardwick | Metaswitch
Vishnu Pavan Beeram | Juniper
Zafar Ali | Cisco
Jeff Tantsura | Ericsson

## Slide 2: Introduction
A YANG data model for the management of PCEP
Includes configuration data and operational state
Base PCEP specification as per RFC 5440 and some extensions
Stateful PCE

## Slide 3: Recent Changes
Last presented in Prague (-03 version); updated based on feedback -
Removed “entity-addr” from all notification
All stats under a container “pcep-stats”
Timestamp for session creation
Description for LSP-DB
Thanks Oscar!

## Slide 4: Stateful PCE's LSP-DB
LSP-DB in PCEP yang with PCEP specific attributes
Generic LSP state in ietf-te
Device specific LSP state in ietf-te-device
add leafref in PCEP yang to ietf-te lsp state

## Slide 5: Stateful PCE's LSP-DB - proposed
leafref to ietf-te

## Slide 6: Open Issue
Mark tunnels to be delegated at PCC in config model
Mark tunnels as PCE-initiated tunnel in config model
Add to ietf-te yang config model?

## Slide 7: Yang Model Arrangement?
Config container has ‘intended-config’
State container has both ‘applied-config’ and ‘derived state
PCEP-Yang
TE-Yang
Follows the OpenConfig suggestion
Maintain ‘intended-config’ and ‘applied-config’ together
Is it upto each module author to decide?

## Slide 8: Next…
PCEP Security
Segment Routing
Association
Including TLS
Request to authors of various extension to help with updating yang model
Add details in manageability considerations for Yang model for ongoing work
Yang: https://github.com/dhruvdhody-huawei/pcep-yang/blob/master/ietf-pcep.yang
PCE WG Adoption call?

## Slide 9: Thanks!