## Slide 1: Ingress Protection What Problem Are We Trying to Solve?
Adrian Farrel
adrian@olddog.co.uk
IETF-95, Buenos Aires, April 2016

## Slide 2: History
Ingress protection has been discussed since at least 2010
  draft-chen-mpls-p2mp-ingress-protection
  draft-torvi-mpls-rsvp-ingress-protection
  draft-ietf-mpls-rsvp-ingress-protection
  draft-ietf-teas-rsvp-ingress-protection
We still have very inconclusive debate about the solutions
  90 minute interim meeting Jan 28th, 2016
    https://www.ietf.org/proceedings/interim/2016/01/28/teas/minutes/minutes-interim-2016-teas-1
Several different solutions offered
Lack of clarity in objectives leads to inability to select one solution

## Slide 3: Objectives Today
Highlight the scope of the problem to be solved
Reach some agreement about what is in scope and what is out of scope
Non-objectives
  Make progress discussing solutions (That is for the proponents of solutions to do)
Beware!
  Some solutions may be better or worse in some scenarios
    Do not pick the problem scope to suit the solution!

## Slide 4: High-Level View – Please Discuss!
Traffic
Traffic
LSP
A “local” failure
  LSP ingress fails
  First hop failure is out of scope
    Can be handled by existing mechanisms (such as FRR)
Objectives
  Continue to deliver traffic
  Minimise repair time
  Re-use network resources
  Minimise steady-state network state

## Slide 5: Traffic Diverted to Another Ingress
Dual-homed CE is definitely in scope
  Allows CE-PE link failure to be in scope as well
Are we considering other cases?
No comment yet on “inside” the network
Traffic
Traffic
LSP
Traffic
Traffic
LSP
CE
PE
PE
Traffic
Traffic
LSP
CE
PE
PE
CE
LSP ingress
LSP ingress

## Slide 6: What Happens Inside the Network?
This is the debate about solutions
  Lots of options
    Bypass tunnel
    MP2P segment
    Segment protection
    End-to-end protection
    Etc., etc., etc.
  Not my objective to resolve this discussion
But…
  It will be helpful if we clarify the objectives…

## Slide 7: Objectives Inside the Network
Don’t contend for resources with the protected LSP
Rapid repair
Scale state in the network
<your requirement here>

## Slide 8: Did Anyone Mention Fault Detection?
Upstream point needs to know how to route traffic
May need to know when to set up repair path
Implies some form of fault detection and propagation
  Considerably dependent on the scenario
  Might not depend on the solution technology