## Slide 1: Extensions to RSVP-TE for LSP Ingress Local Protection
draft-ietf-teas-rsvp-ingress-protection-05
Huaimo Chen, Raveendra Torvi
Ning So, Autumn Liu, Yimin Shen
Tarek Saad, Fengman Xu
Mehmet Toy, Lei Liu
Renwei Li, Quintin Zhao
Zhenbin Li, Boris Zhang, Markus Jork

## Slide 2: Contents
Address some comments
Problem Summary
Objectives and Scope

## Slide 3: Address comments
For ingress and backup ingress not adjacent
Configure a tunnel between primary ingress and backup ingress if they are not one hop away
Can Linear Protection protect ingress of LSP?
  No
LER-Z
LER-A
Working LSP
Protection LSP
LER-A: Ingress of working LSP and Protection LSP
P1
P3
P2
Linear Protection:
LER-A (Ingress) switches traffic to Protection LSP when failure happens on Working LSP.

## Slide 4: Problem Summary
Need for fast, efficient protection for ingress of LSP (P2MP or P2P LSP)
Existing solution: Two end to end P2MP/P2P LSPs
  Consumes lots of network resources (Double states need to be maintained in the network since two end to end TE LSPs are created. Double link bandwidth is reserved and used when both the primary and the secondary end to end TE LSPs carry the traffic at the same time)
  More operations (configurations of two end to end TE LSPs and BFDs from each of the egress nodes to its corresponding ingress node)
  Detection of ingress failure may not be reliable
  Speed of protection against ingress failure may be slow

## Slide 5: Objectives and Scope
Objectives
  Fast protection for ingress
  (minimize traffic interruption when ingress fails)
  Efficient protection for ingress
  (minimize usage of network resources, including memory for states and link bandwidth)
  Simple operations
Scope
  Local Protection/Repair for Ingress
  (Not end to end protection)
  (Not for links attached to ingress)

## Slide 6: Thanks
Any comments?

## Slide 7: Existing P2MP LSP Ingress & Egress Protections
Multicast
Source
Multicast
Receiver
Data
PE2
PE1
PE10
PE9
CE2
CE1
CE4
CE1
Primary P2MP LSP
Backup P2MP LSP
Data
PE7
PE8
CE3
PE3
PE4
PE5
PE6
1. Two P2MP LSP carry data
2. P2P LSP (leafroot) with BFD
3. P2P LSP as NH to SA, export route for SA to receiver (when PE1 fails, route withdrawn)
4. CE3 selects leaf according to route to SA
P2P LSP

## Slide 8: P2P LSP Ingress & Egress Protections
PE2
PE1
CE1
CE1
Primary P2P LSP
Backup P2P LSP
Data
PE7
PE8
CE3
1. Two P2P LSP carry data
2. P2P LSP (egressingress) with BFD
3. P2P LSP as NH to SA, export route for SA to receiver (when PE1 fails, route withdrawn)
4. CE3 selects an egress according to route to SA
P2P LSP

## Slide 9: P2P LSP Ingress & Egress Protections
PE2
PE1
CE1
CE1
Primary P2P LSP
Backup P2P LSP
Data
PE7
PE8
CE3
1. Two P2P LSP One carries data
2. FRR for links and transit nodes
4. CE1 needs to detect egress failure and switch traffic to backup LSP
3. CE3 receives data from both

## Slide 10: Extensions to RSVP-TE for LSP Egress Local Protection
draft-ietf-teas-rsvp-egress-protection-04
Huaimo Chen, Autumn Liu
Tarek Saad, Fengman Xu
Lu Huang, Ning So
Mehmet Toy, Lei Liu, Zhenbin Li
Boris Zhang, Nan Meng, Vic Liu

## Slide 11: Contents
Re-use and extend SERO (to replace EGRESS_BACKUP object)
Enhance on operations

## Slide 12: Re-use and Extend SERO
Secondary Explicit Route object (SERO) in RFC 4873
Its format is re-used
Some contents are extended/changed
SERO in RFC 4873
Branch node subobject
Protection subobject
Merge node subobject
SERO for egress protection
Branch node subobject (PH of egress)
Protection subobject extended
Backup egress node subobject
Contents of protection subobject is extended below (PROTECTION object is extended in same way)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|L| Type | Length | Reserved | C-Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|S|P|N|O| Reserved | LSP Flags | Reserved | Link Flags|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|I|R| Reserved | Seg.Flags | Reserved |E-Flags|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional subobjects ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Contents of protection subobject

## Slide 13: Enhance on Operations
PE1
CE1
Primary LSP
Backup LSP
Data
PE7
PE8
CE3
1. Configure Backup Egress on ingress
3. Configure Backup Egress on primary egress
Backup Egress
Primary Egress
Ingress
P2
P1
2. Configure same IP address on primary backup egress and backup egress
2. Configure same IP address on primary backup egress and backup egress
Only one of three configurations is used (1 and 2: existing, 3: new)
For 1, SERO w/ PE8 in Path to P2, creating backup LSP from P2 to PE8
For 2, P2 determines backup egress PE8, creates backup LSP to PE8
For 3, SERO w/ PE8 as backup egress in Resv to P2 from PE7, P2 creates backup LSP from P2 to PE8.

## Slide 14: Thanks
Any comments?

## Slide 15: E-Flags and Optional Subobjects
E-Flags:
  x01: Egress local protection
  x02: Other sending UA label (existing in previous version)
  X04: S2L sub LSP backup desired (existing)
Optional Subobjects:
  Primary Egress
  P2P LSP ID (Existing in previous version)
  Opaque Data (Generalized from previous version)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IPv4 address (of primary egress) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
IPv4 Primary Egress subobject
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Opaque Data |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Opaque Data subobject