## Slide 1: Yang Data Model for TE Topologies draft-ietf-teas-yang-te-topo-04 Github: https://github.com/ietf-mpls-yang/te/blob/master/ietf-te-topology.yang
Xufeng Liu (Ericsson)
Vishnu Pavan Beeram (Juniper Networks)
Igor Bryskin (Huawei Technologies)
Tarek Saad (Cisco)
Himanshu Shah (Ciena)
Oscar Gonzalez De Dios (Telefonica)
Contributors:
Sergio Belotti (Alcatel-Lucent)
Diete Beller (Alcatel-Lucent)
draft-ietf-teas-yang-te-topo-04

## Slide 2: Summary of Changes
Alignment with new I2RS network topology model (version 2015-12-09).
Submitted separate draft for schedule.
Split the packet attributes to an augmentation module.
In node, added alt-information-sources.
Support for request containing multiple topologies from client to provider. Added an attribute "preference" in topology.
Alignment with L3 network topology model.
Worked with TE Yang model DT to align TE Tunnel modeling.
Added support for tunnel termination point.
draft-ietf-teas-yang-te-topo-04

## Slide 3: Alignment with New I2RS Network Topology Model
draft-ietf-teas-yang-te-topo-04
augment /nw:networks:
+--rw te!
+--rw templates
augment /nw:networks/nw:network:
+--rw te!
+--rw provider-id te-global-id
+--rw client-id te-global-id
+--rw te-topology-id te-topology-id
+--rw config
+--ro state
augment /nw:networks/nw:network/nw:node:
+--rw te!
+--rw te-node-id te-node-id
+--rw config
+--ro state augment /nw:networks/nw:network/nt:link:
+--rw te!
+--rw config
+--ro state
module: ietf-network
+--rw networks
| +--rw network* [network-id]
| +--rw network-types
| +--rw network-id network-id
| +--rw supporting-network* [network-ref]
| | +--rw network-ref leafref
| +--rw node* [node-id]
| +--rw node-id node-id
| +--rw supporting-node* [network-ref node-ref]
| +--rw network-ref leafref
| +--rw node-ref leafref

## Slide 4: Submitted Separate Draft for Schedule
Submitted draft-liu-netmod-yang-schedule-00
  Has wider applicability.
  Will present it to Netmod working group.
draft-ietf-teas-yang-te-topo-04

## Slide 5: Split the Packet Attributes to an Augmentation Module
Base TE Topology Model Is Technology Agnostic
  Packet switching model augments base model.
  Packet switching model covers packet switch attributes.
draft-ietf-teas-yang-te-topo-04
module: ietf-te-topology-psc
Augment /nw:networks/nw:network/nt:link/tet:te/tet:config/tet:te-link-attributes/tet:interface-switching-capability:
+--rw packet-switch-capable
+--rw minimum-lsp-bandwidth? decimal64
+--rw interface-mtu? Uint16
augment /nw:networks/nw:network/nt:link/tet:te/tet:state/tet:te-link-attributes/tet:interface-switching-capability:
+--ro packet-switch-capable
+--ro minimum-lsp-bandwidth? decimal64
+--ro interface-mtu? Uint16
augment /nw:networks/nw:network/nt:link/tet:te/tet:state/tet:alt-information-sources/tet:interface-switching-capability:
+--ro packet-switch-capable
+--ro minimum-lsp-bandwidth? decimal64
+--ro interface-mtu? uint16
augment /tet:te-link-event/tet:te-link-attributes/tet:interface-switching-capability:
+---- packet-switch-capable
+---- minimum-lsp-bandwidth? decimal64
+---- interface-mtu? uint16

## Slide 6: In Node, Added alt-information-sources
draft-ietf-teas-yang-te-topo-04
augment /nw:networks/nw:network/nw:node:
+--rw te!
+--ro state
| +--ro information-source? enumeration
| +--ro information-source-state
| | +--ro credibility-preference? uint16
| | +--ro topology
| | | +--ro provider-id-ref? leafref
| | | +--ro client-id-ref? leafref
| | | +--ro te-topology-id-ref? leafref
| | | +--ro network-id-ref? leafref
| | +--ro routing-instance? string
| +--ro alt-information-sources* [information-source]

## Slide 7: Support for Request Containing Multiple Topologies from Client to Provider
Added an attribute "preference" in topology.
draft-ietf-teas-yang-te-topo-04
module: ietf-te-topology
augment /nw:networks/nw:network:
+--rw te!
+--rw config
| +--rw preference? uint8

## Slide 8: Alignment with L3 Network Topology Model
Submitted separate draft draft-liu-teas-yang-l3-te-topo-00.
draft-ietf-teas-yang-te-topo-04
module: ietf-l3-te-topology
augment /nw:networks/nw:network/nw:network-types/l3t:l3-unicast-igp-topology:
+--rw l3-te!
augment /nw:networks/nw:network/l3t:igp-topology-attributes:
+--rw l3-te-topology-attributes
+--rw network-ref? leafref
augment /nw:networks/nw:network/nw:node/l3t:igp-node-attributes:
+--rw l3-te-node-attributes
+--rw node-ref? leafref
+--rw network-ref? leafref
augment /nw:networks/nw:network/nw:node/nt:termination-point/l3t:igp-termination-point-attributes:
+--rw l3-te-tp-attributes
+--rw tp-ref? leafref
+--rw node-ref? leafref
+--rw network-ref? leafref
augment /nw:networks/nw:network/nt:link/l3t:igp-link-attributes:
+--rw l3-te-link-attributes
+--rw link-ref? leafref
+--rw network-ref? leafref

## Slide 9: Worked with TE Yang Model DT to Align TE Tunnel Modeling
draft-ietf-teas-yang-te-topo-04
Both models can be on either device or controller.
Both models share the same terminologies and types.
Both models cross reference each other whenever needed.

## Slide 10: Support for Tunnel Termination Point
draft-ietf-teas-yang-te-topo-04
module: ietf-te-topology
augment /nw:networks/nw:network/nw:node:
+--rw te!
+--rw te-node-id te-node-id
+--rw tunnel-termination-point* [tunnel-tp-id]
+--rw tunnel-tp-id binary
+--ro state
+--ro switching-capability? identityref
+--ro encoding? identityref
+--ro termination-capability* [link-tp]
+--ro link-tp leafref

## Slide 11: Modeling Abstractions
draft-ietf-teas-yang-te-topo-01
N3
client layer
server layer
EP11
N1
N2
N4
EP61
N6
N5
TTP
LTP
TE Tunnel
TE Link
TE Node

## Slide 12: Modeling Abstractions
draft-ietf-teas-yang-te-topo-04
Abstraction
Network Facing Line Card
Termination Device with Client Ports
Blocking Switching component
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)

## Slide 13: Modeling Abstractions
draft-ietf-teas-yang-te-topo-04
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
Link-12
Link-23
Node-2
Node-3
Node-1
TE-Tunnel-1

## Slide 14: Multi-layer Transformations
draft-ietf-teas-yang-te-topo-04
N3
client layer
server layer
EP11
N1
N2
N4
EP61
N6
N5
client layer link
TTP

## Slide 15: Multi-layer Transformations
draft-ietf-teas-yang-te-topo-04
Tunnel Termination Point (TTP)
Server Link Termination Point (LTP)
Client Link Termination Point (LTP)
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
Link-12
Link-23
Node-2
Node-3
Node-1
TE-Tunnel-1
Client Layer TE Link

## Slide 16: Option 1: Transitional Link
draft-ietf-teas-yang-te-topo-04

## Slide 17: Option 1: Transitional Link
draft-ietf-teas-yang-te-topo-04
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-3
C-LTP-1,2,3
C-LTP-4,5,6
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-3
C-LTP-1,2,3
C-LTP-4,5,6
Transformation
Logical Sub-node
Transitional Link
Logical TP
Layer 1
Layer 2

## Slide 18: Option 1: Transitional Link
draft-ietf-teas-yang-te-topo-04
Decompose one node into two logical nodes.
Treat Tunnel TP the same as Link TP.
Modeling changes:
  On Link TP: need to have an attribute for switch-layer.
  On Link: have a flag to indicate the link is transitional.

## Slide 19: Option 1: Transitional Link
draft-ietf-teas-yang-te-topo-04
Transition links are going across layers, asking path computations on both layer to be aware.
Causing a more complex topology, because the additional nodes and links, in mixed layers.
Need a mechanism to decompose nodes, generate links and assign attributes.
Existing TE link attributes are not applicable to transition links.

## Slide 20: Option 2: Inter-layer Locks
IL-3
draft-ietf-teas-yang-te-topo-04
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
Describe client-server layer adaptation relationship.
It is an association of M client layer LTPs and N server layer TTPs.
Each association is uniquely identified by an inter-layer lock ID.
IL-1
IL-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-3
C-LTP-1,2,3
C-LTP-4,5,6
TTP1 | IL-1 | C-LTP-1 | IL-1
TTP2 | IL-2, IL-3 | C-LTP-2 | IL-1
TTP3 | IL-2 | C-LTP-3 | IL-1
 |  | C-LTP-4 | IL-2
 |  | C-LTP-5 | IL-2
 |  | C-LTP-6 | IL-3

## Slide 21: Option 2: Inter-layer Locks
draft-ietf-teas-yang-te-topo-04
Do not decompose nodes.
Modeling changes:
  On Link TP and TTP: add an attribute for inter-layer-lock-id.
Inter-layer properties are separate and independent from TE links, having different attributes from TE link attributes.
Inter-layer properties are used only for multi-layer, not for single layer cases.

## Slide 22: Modeling Considerations
draft-ietf-teas-yang-te-topo-04
The inter-layer lock approach and transition-link approach can both be supported at the same time.
The two approaches can co-exist, with some parts of the system modeled by one approach and other parts modeled by another approach.

## Slide 23: Topology Layer Separation
draft-ietf-teas-yang-te-topo-04
Besides putting multiple layers into one topology, TE topology model allows to separate server and client layer networks into two independent TE topologies.

## Slide 24: Topology Layer Separation
draft-ietf-teas-yang-te-topo-04
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
Link-12
Link-23
Node-2
Node-3
Node-1
TE-Tunnel-1
Client Layer TE Link

## Slide 25: Topology Layer Separation
draft-ietf-teas-yang-te-topo-04
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
Link-12
Link-23
Node-2
Node-3
Node-1
TE-Tunnel-1
Client Layer TE Link
LTP-11
LTP-12
LTP-21
LTP-22

## Slide 26: Topology Layer Separation
draft-ietf-teas-yang-te-topo-04
In such a case, a transitional link cannot be used between LTP-11 and TTP-1.

## Slide 27: Next Steps
draft-ietf-teas-yang-te-topo-02
Address review comments.
  To Do List:
    https://github.com/ietf-mpls-yang/te/blob/master/ietf-te-topology-todo-list.txt
Request further review.