## Slide 1: RSVP Extensions For Re-optimization of Loosely Routed Point-to-Multipoint Traffic Engineering Label Switched Paths (LSPs) draft-ietf-teas-p2mp-loose-path-reopt-05
Author list:
  Tarek Saad (tsaad@cisco.com)
  Rakesh Gandhi (rgandhi@cisco.com) - Presenter
  Zafar Ali (zali@cisco.com)
  Robert H. Venator (robert.h.venator.civ@mail.mil)
  Yuji Kamite (y.kamite@ntt.com)
95th IETF, TEAS WG, Buenos Aires (April 2016)

## Slide 2: Outline
Requirement
Recent Update
Next Steps

## Slide 3: Requirement
P2MP-TE LSP [RFC4875]
Loosely routed LSP re-optimization [RFC4736]
As per P2MP-TE [RFC4875], an LSR may:
  Re-optimize the entire P2MP-TE LSP by resignaling all its S2L sub-LSP(s), i.e. all destinations.
  Combine multiple Path/PathErr messages using S2L sub-LSP descriptor-list to alleviate scale issue.
  A combined message with large number of S2L sub-LSPs in the descriptor-list may be fragmented by the sender and arrive out of order at the receiver.

## Slide 4: Outline
Requirement
Recent Update
Next Steps

## Slide 5: S2L_SUB_LSP_FRAG Object Format
S2L_SUB_LSP_FRAG: Class-Num 50, C-Type TBA by IANA
+-----------------------+-----------------------+-----------------------+-------------------------+
| Len (12 bytes) | Class_Num 50 | SUB_LSP_FRAG |
+-----------------------+-----------------------+-----------------------+-------------------------+
| Reserved | Fragment ID |
+-----------------------+-----------------------+-----------------------+-------------------------+
| Fragments Total | Fragment Number |
+-----------------------+-----------------------+-----------------------+-------------------------+
Fragment ID: 16-bit integer in the range of 1 to 65535. This value is incremented for each new RSVP message that needs to be fragmented.
Fragments Total: 16-bit integer in the range of 1 to 65535. This value indicates the number of fragments sent for the given RSVP message.
Fragment Number: 16-bit integer in the range of 1 to 65535. This value identifies the specific fragment of the original packet.
The S2L_SUB_LSP_FRAG Object is added before adding the S2L_SUB_LSP_IPv4 or S2L_SUB_LSP_IPv6 Object in the fragmented message.

## Slide 6: Fragmented Path Messages with S2L_SUB_LSP_FRAG Object
<Path Message Frag-1> ::= <Common Header> [ <INTEGRITY> ]
<SESSION> <RSVP_HOP>
[ <EXPLICIT_ROUTE> ] ….
<sender descriptor>
<S2L sub-LSP descriptor list-1>]
<Path Message Frag-N> ::= <Common Header> [ <INTEGRITY> ]
<SESSION> <RSVP_HOP>
[ <EXPLICIT_ROUTE> ] ….
<sender descriptor>
<S2L sub-LSP descriptor list-N>]
Format of S2L sub-LSP descriptor-list:
<S2L sub-LSP descriptor list> ::= <S2L_SUB_LSP_FRAG> <S2L sub-LSP descriptor>
[ <S2L sub-LSP descriptor list> ]
<S2L sub-LSP descriptor> ::= <S2L_SUB_LSP>
[ <P2MP SECONDARY_EXPLICIT_ROUTE> ]

## Slide 7: S2L_SUB_LSP_FRAG Object Usage
LSR adds optional S2L_SUB_LSP_FRAG Object with a sub-set of S2L sub-LSP descriptor list(s) in each Path/PathErr message fragment.
  A mid-point LSR SHOULD wait to accumulate all fragments and put them in-order before attempting to re-evaluate preferable path when a Path message with "Path Re-evaluation Request" is received.
  An ingress node SHOULD wait to accumulate all fragments and put them in-order before attempting to trigger re-optimization when a PathErr message with "Preferable Path Exists" is received.

## Slide 8: Outline
Requirement
Recent Update
Next Steps

## Slide 9: Next Steps
Document is updated to address review comments from Pavan
Welcome comments from the WG on the document especially on the changes presented today
IPR poll was completed for the WG LC
Requesting WG LC

## Slide 10
Thank You.