## Slide 1: Framework for Abstraction and Control of Transport Networks
draft-ceccarelli-teas-actn-framework-01
IETF 95 – Buenos Aires
Daniele Ceccarelli (Ericsson)
Young Lee (Huawei)
Daniel King (Lancaster-University)
Sergio Belotti (Alcatel-Lucent)
Luyuan Fang (Microsoft)
Dhruv Dhody (Huawei)
Diego Lopez (Telefonica)

## Slide 2: Draft-status
New terminology section
New section describing the VN creation phases
New section introducing the concepts of
  Access Point
  Virtual Network Access Point
New section describing virtual end point mobility

## Slide 3: VN creation process: abstraction level
Topology Abstraction Level
No abstraction: Black
Total abstraction: white
Shades of grey

## Slide 4: VN creation process: phases
Negotiation (optional): In the case of “shades of grey” topology abstraction, there is an a priori phase in which the customer agrees with the provider on the type of topology to be shown, e.q. 10 virtual links and 5 virtual nodes with a given interconnectivity. This is something that is assumed to be preconfigured by the operator off-line, what is online is the capability of modifying/deleting something (e.g. a virtual link). In the case of "white" abstraction this negotiation phase does not happen. Only access points are shown.
Implementation: In the case of white topology abstraction, the customers can ask for connectivity with given constraints/SLA between his own access points and LSPs/tunnels are created by the provider to satisfy the request. What the customer sees is only that his CE are connected with a given SLA. In the case of “shades of grey” the customer creates his own LSPs as he wants accordingly with the topology that was presented to him.

## Slide 5: Access Point - Before VN creation
CE1
Domain 1
Domain 3
CE2
1.A
1.B
3.A
3.B
CE3
AP1
AP3
2.A
AP Id | MaxResBwd | Total Bwd | CE, port
AP1 | 20Gb | 20Gb | CE1, portX
AP2 | 10Gb | 10Gb | CE2, portY
AP3 | 100Gb | 100Gb | CE3, portX
AP2
Customer View
AP Id | MaxResBwd | Total Bwd | PE, port
AP1 | 20Gb | 20Gb | 1.A, portX
AP2 | 10Gb | 10Gb | 2.A, portY
AP3 | 100Gb | 100Gb | 3.B, portX
Operator View

## Slide 6: After creation of VN red and blue
CE1
Domain 1
Domain 3
CE2
1.A
1.B
3.A
3.B
CE3
AP1
-VNAP1.9 (1Gb)
-VNAP1.5 (2Gb)
AP3
-VNAP3.9 (100Mb)
-VNAP3.5 (2Gb)
2.A
AP2
-VNAP2.9 (1Gb)
-VNAP2.5 (2Gb)
VN red:ID=9
AP Id | MaxResBw | Total Bw | CE, port
AP1 | 17Gb | 20Gb | CE1, portX
-VNAP1.9 |  | 1Gb | 
-VNAP1.5 |  | 2Gb | 
AP2 | 7Gb | 10Gb | CE2, portY
-VNAP2.9 |  | 1Gb | 
-VNAP2.5 |  | 2Gb | 
AP3 | 97.9Gb | 100Gb | CE3, portX
-VNAP3.9 |  | 100Mb | 
-VNAP3.5 |  | 2Gb | 
VN blue:ID=5
Notes: VNAPx.y: Virtual Network Access Point. It is used to reserve on AP X the resource related to VN Y. It is created along with the creation of the VN. 1 VNAP correspond to 1 VN. Multiple VNAP are allowed on an AP.
AP id=VN id
ceIP (optional)
peIP (optional)
total bw

## Slide 7: End point mobility
End point mobility
  I need connectivity between site A and a function that can be deployed in X, Y, Z. Please tell me which to use accordingly to my constraints, polices and network status.
  The best is A-Y (setup and notification to CNC)
End point mobility preplanned
  See draft
End point mobility on the fly
  See draft
PNC
PNC
MDSC
CNC
A
1
1
X
Y
Z
2
2

## Slide 8: Other open issues
AP: better definition needed
VNAP: needed for dual homing and bandwidth reservation on access links. Better definition?
MDSC to PNC relationship
  1:N (Default)
  M:1
  M:N (Work Load Partitioning)
…

## Slide 9: Next Steps
Keep alignment with requirements draft and info model draft
Refine AP and VNAP concepts
WG adoption