## Slide 1: RSVP-TE Extensions for Associated Co-routed Bidirectional Label Switched Paths (LSPs) draft-gandhishah-teas-assoc-corouted-bidir-01
Author list:
  Rakesh Gandhi, Cisco Systems (rgandhi@cisco.com) - Presenter
  Himanshu Shah, Ciena (hshah@ciena.com)
  Jeremy Whittaker, Verizon (jeremy.whittaker@verizon.com)
95th IETF, TEAS WG, Buenos Aires (April-2016)

## Slide 2: Outline
Requirements
Problem Statement
Signaling Procedure
Next Steps

## Slide 3: Requirements
This draft addresses following packet transport network requirements:
  Co-routed Bidirectional LSP, where reverse LSP follows the same path as its forward LSP
  Take advantage of the existing TE mechanisms deployed in the network
  Without having to migrate to GMPLS signaling in the network

## Slide 4: Problem Statement
Associate two reverse co-routed unidirectional LSPs unambiguously to form a co-routed bidirectional LSP
Ensure revere LSP traverses the same path as its forward LSP
Fast Reroute mechanisms to ensure traffic flows on a co-routed path after a failure on the LSP

## Slide 5: Signaling Procedure - I
Associate two reverse co-routed LSPs using following mechanisms:
  Single-sided provisioning, as defined in RFC7551
    Remote side triggers the reverse LSP using the Path message received in the forward LSP
  Use of EXTENDED ASSOCIATION Object to associate two LSPs unambiguously at mid-points:
    Extended Association ID carries originating (forward) LSP source address and source-port (LSP-ID) for unique identification.
      As EXTENDED_ASSOCIATION Object is copied in the reverse LSP, it has a pointer to the originating LSP.
    COROUTED-LSP flag to indicate LSPs are co-routed.

## Slide 6: Signaling Procedure - II
Ensure revere LSP traverses the same path as its forward LSP
  Originating LSP carries an EXPLICIT_ROUTE Object (ERO) for the co-routed reverse LSP in the REVERSE_LSP Object
  When using loose next-hop(s), originating LSP carries RECORD_ROUTE Object (RRO) to record its path, which is then used by the reverse LSP to ensure it is co-routed

## Slide 7: Signaling Procedure - III
Fast reroute using mechanisms defined in draft-ietf-teas-gmpls-lsp-fastreroute:
  BYPASS_ASSIGNMENT subobject in RRO is used to co-ordinate bypass tunnel assignment between forward and reverse direction Point of Local Repair (PLR) nodes.
  After a failure, both sides independently follow the fast reroute procedures defined in RFC4090.
  Re-corouting procedure is used to ensure traffic follows co-routed path after the failure.
  COROUTED-LSP flag is used by the PLR to assign co-routed bypass.

## Slide 8: Next Steps
Small extensions for RFC7551 and draft-ietf-teas-gmpls-lsp-fastreroute
Welcome review comments and suggestions
Like to request WG adoption

## Slide 9
Thank You.