## Slide 1: Transmission of IP Packets over IEEE 802.11 in mode Outside the Context of a Basic Service Set
draft-petrescu-ipv6-over-80211p-05.txt
A. Petrescu (speaker),
N. Benamar, J. Härri, C. Huitema, J-H. Lee, T. Ernst, T. Li
Special thanks to François Simon
IETF Seoul, November 15th, 2016

## Slide 2: Contents
Progress since Berlin
Current Issues
Next steps

## Slide 3: Progress since Berlin
Joined four drafts:
  draft-petrescu-ipv6-over-80211p-04.txt
  draft-ernst-its-ipv6-over-80211ocb-00.txt
  draft-lee-its-ipv6-over-80211ocb-00.txt
  draft-haerri-ipv6-over-80211ocb-00.txt
Addressed the comments from Berlin BoF:
  Changed title
  Improved MTU text
  Improved “Qos Data Header” vs “Data Header”
  Improved text of multicast address mapping
Proposed IPv4 text
Improved some text and some figures

## Slide 4: Title
Transmission of IP Packets over IEEE 802.11 in mode Outside the Context of a Basic Service Set
  good but does not sound perfect

## Slide 5: MTU
Default MTU is 1500 bytes, as in IPv6-over-Ethernet (RFC2464)
New from RFC2464:
  If packets larger than 1500 bytes then IP layer fragments into multiple IP fragments
    The “Seq No” of the “IEEE 802.11 Data” header of subsequent IP fragments is incremented
  It is possible to send packets bigger than MTU, without producing fragments (previously set a larger than 1500bytes MTU parameter on the interface), but there may be Packet Too Big replies from the Router (if it has not set it too).
  It is possible to set the MTU on an interface smaller than 1500bytes (the minimum is 255bytes).

## Slide 6: MTU (continued)
New from RFC2464:
  It is possible that the MAC layer fragments as well (L2 fields “Fragment Number” and “More Fragments”); but was never experimented.
  It is possible that the app-layer fragments.
  Non-IP packets, such as geonet have an MTU of 1492bytes, and WSMP have no limits
  Equivalent Transmit Time on Channel concept

## Slide 7: “802.11 Data” vs “802.11 QoS Data” headers
IPv6 packets can be transmitted as "IEEE 802.11 Data" or alternatively as "IEEE 802.11 QoS Data".
IEEE 802.11 Data IEEE 802.11 QoS Data
Logical-Link Control Logical-Link Control
IPv6 Header IPv6 Header
The value of the field "Type/Subtype" in the 802.11 Data header is 0x0020.
The value of the field "Type/Subtype" in the 802.11 QoS header is 0x0028.

## Slide 8: Address Mapping – Multicast
0x3333 is the value of the first two octets of the MAC address
  0x3333 is not listed at IEEE, yet it’s widely used
Alternatively, consider the other values listed at IEEE https://standards.ieee.org/develop/regauth/grpmac/public.html

## Slide 9: IPv4 proposed text
Title says “IP” instead of “IPv6”, and other section titles modified accordingly.
RFC894 “IPv4 over Ethernet”
RFC826 “ARP”
EtherType 0x0800
IPv4 Link-local addresses RFC

## Slide 10: Current Issues (1)
Some editing needed
  re-arrange sections
  move down or simply out some sections
  document should be shortened
  some text is repeated
  typos and expression improvements
  mention ND impacts
  move packet capture to annex
  MAC addresses pose risks also in non-vehicular environments (e.g. in 802.11)
  more terms definitions needed like OBU, WSMP, more.
  “Design Considerations” title is too generic and should be more specific
  need figure captions
  explain the frame type bitfield in the figure
  adaptation layer ignores the radiotap header, yes
  …

## Slide 11: Current Issues (2)
The inclusion or exclusion of IPv4 text. Options:
  Not needed at all
  Needed inside this document
  Needed in a separate document
Selected pro/con arguments
  Charter is IPv6
  Numerous IPv4 trials, some industry reqs
  Doc mgmt. easiness
  Past example RFC5154 “_IP_ over 802.16” (v4 and v6)
  IEEE P1609.3 and ETSI ITS-G5 are _only_ IPv6
  IPv4 carried in IPv6 packets

## Slide 12: Current Issues (3)
Concern about repeating text from RFC2464

## Slide 13: Current Issues (4)
  section 6.5 “Stateless Autoconf” : “For example, the Interface Identifier for an 802.11p interface whose built-in address is, in hexadecimal: 30-14-4A-D9-F9-6C would be 32-14-4A-FF-FE-D9-F9-6C.”
  Suggestion from commenter: get rid of text in 6.5, and refer to RFC4862 and RFC7721 “Security and Privacy Considerations for IPv6 Address Generation Mechanisms”.
  Refer also to the ‘U/G’ bits RFC.
  Align with draft-ietf-6man-default-iids

## Slide 14: Current Issues (5)
Also in section 4, there is an introduction of the OCB mode in section 4:
  But vehicles will alternate between OCB mode, in which there is no infrastructure support, and some form of connected mode, in which there is.
    Should be clarified.

## Slide 15: Current Issues (6)
In section 5.5. Authentication requirements, there is a request that “IPv6 over 802.11-OCB packets must contain a certificate.” This seems strange. Vehicle communication may be using short certificates today, but we are headed towards post-quantum cryptography, in which certificates will not possibly fit in a single packet. There is an obvious security requirement, but it should apply to the design of OCB applications, rather than packet transmission itself. We should clarify the text and explain that this is a requirement to the layer above IPv6.

## Slide 16: Current Issues (7)
Section 6.3. Link-Local Addresses states that “For IPv4, link-local addressing is described in [RFC3927].” That’s a true statement, but RFC3927 describes picking random numbers in 169.254/16, with a high probability of collision if more than 100 vehicles share the same OCB neighborhood. We may want to expand on that in the next revision.

## Slide 17: Current Issues (8)
Section 6.4.2. Address Mapping – Multicast is a restatement of RFC 2464 section 7.
Should not repeat text.
Maybe “additional multicast scopes”
“all-yellow-taxis-in-street” looks more like the definition of a multicast group than the definition of a multicast scope. Are we sure that we want to define an actual scope, parallel with “link local”, “site local” and “global”, versus just a specific global scope multicast group?

## Slide 18: Current Issues (9)
1) We must change our MAC address, and the embedded version in the IPv6 (and IPv4) address, and in general also any Application ID (or layer ID) that could breach privacy
2) We are not in control on when changing our MAC address. If IEEE WAVE (BSM being sent) is running in parallel, then it should be IEEE WAVE triggering their pseudonym change AND ours.

## Slide 19: Current Issues (10)
Section 6.6. Subnet Structure.
replace the text “The 802.11p networks, much like other 802.11 networks,” by a simpler “The 802.11p networks in OCB mode.”
(because risk of controversy with most 802.11 being infrastructure mode)

## Slide 20: Current Issues (11)
IEEE about to make a protocol change to “LLC”, and we talk in our draft extensively about “LLC Header” (stacks, adaptation layer, etc.)
“There are two LLC sublayer protocols used (see IEEE Std 802-2014 (Overview and Architecture)): LLC Protocol Discrimination (LPD) (see ISO/IEC 8802-2:1998) and EtherType Protocol Discrimination (EPD) (see IEEE Std 802.3-2012). LPD is used for transmission of all IEEE Std 802.11 MSDUs with the exception of the 5.9 GHz bands where EPD is used (see E.2.3 (5.9 GHz band in the United States (5.850–5.925 GHz)) and E.2.4 (5.9 GHz band in Europe (5.855–5.925 GHz))). When LPD is used, …”
Suggestion:
  refer the origin of 802.11 OCB (from 802.11p-2010) only once, and never mention "802.11p" again.
  insert "in the next release of 802.11 standard, the LLC is based on 802-2014“
    Suggest the Wireshark implementer to talk about LPD and EPD as kinds of LLC.

## Slide 21: Current Issues (12)
This WG is named “IPWAVE”
The WAVE part is confusing during IEEE conversation about LLC
Suggestion: write a lowercase “ipwave” instead.
  This is not an issue of the IPv6-over-802.11-OCB document

## Slide 22: Current Issues (13)
<empty>

## Slide 23: Current Issues (14)
How can an MTU be lower than 500? Compliance to RFC2460?

## Slide 24: Current Issues (15)
Irrelevance of text about MAC and app-layer fragmentation, as this is transparent to IP.
  Yes, but there is a field in the MAC header which is updated when IP performs fragmentation
  Yes, but there is an option to the ping application which triggers IP to make fragments.

## Slide 25: Current Issues (16)
IP handover performance: need analysis of OCB link crowding with too frequent RAs (needed to improve IP handover performance)

## Slide 26: Current Issues (17)
Avoid the text in the “Subnet Structure” section altogether
  ? refer to RFC5889 “addressing model for ad-hoc networks”, draft-baccelli-multi-hop-wireless-communication-06

## Slide 27: Current Isues (18)
Multicast issues in 802.11 are even more relevant in OCB mode.
  Maybe refer to draft-perkins-intarea-multicast-ieee802-01?

## Slide 28: Current Issues (19)
What are the differences between "IEEE 802.11 Data" and "IEEE 802.11 QoS Data“:
  Explain the differences

## Slide 29: Current Issues (20)
Appendix D “Use of IPv6-over-802.11-OCB for distribution of certificates” – is not in scope of this document
  Should be moved out, to what document?