## Slide 1: Transmission of IP Packets over IEEE 802.11 in mode Outside the Context of a Basic Service Set
draft-petrescu-ipv6-over-80211p-05.txt
A. Petrescu (speaker),
N. Benamar, J. Härri, C. Huitema, J-H. Lee, T. Ernst, T. Li
Special thanks to François Simon
IETF Seoul, November 15th, 2016

## Slide 2: Contents
Progress since Berlin
Issues needing resolution
Solved Issues

## Slide 3: Progress since Berlin
Merged four drafts:
  draft-petrescu-ipv6-over-80211p-04.txt
  draft-ernst-its-ipv6-over-80211ocb-00.txt
  draft-lee-its-ipv6-over-80211ocb-00.txt
  draft-haerri-ipv6-over-80211ocb-00.txt
Addressed the comments from Berlin BoF:
  Changed title
  Improved MTU text
  Improved “Qos Data Header” vs “Data Header”
  Improved text of multicast address mapping
Proposed IPv4 text
Improved some text and some figures

## Slide 4: Title
Transmission of IP Packets over IEEE 802.11 in mode Outside the Context of a Basic Service Set
  good but does not sound perfect

## Slide 5: IPv4 proposed text
Title says “IP” instead of “IPv6”, and other section titles modified accordingly.
RFC894 “IPv4 over Ethernet”
RFC826 “ARP”
EtherType 0x0800
IPv4 Link-local addresses RFC

## Slide 6: Issues (1)
The inclusion or exclusion of IPv4 text. Options:
  Not needed at all
  Needed inside this document
  Needed in a separate document
Selected pro/con arguments
  Charter is IPv6
  Numerous IPv4 trials, some industry reqs
  Doc mgmt. easiness
  Past example RFC5154 “_IP_ over 802.16” (v4 and v6)
  IEEE P1609.3 and ETSI ITS-G5 are _only_ IPv6
  IPv4 carried in IPv6 packets

## Slide 7: Issues (2)
Section 6.3. Link-Local Addresses states that “For IPv4, link-local addressing is described in [RFC3927].” That’s a true statement, but RFC3927 describes picking random numbers in 169.254/16, with a high probability of collision if more than 100 vehicles share the same OCB neighborhood. We may want to expand on that in the next revision.
  Depends on the IPv4 decision

## Slide 8: “802.11 Data” vs “802.11 QoS Data” headers
IPv6 packets can be transmitted as "IEEE 802.11 Data" or alternatively as "IEEE 802.11 QoS Data".
IEEE 802.11 Data IEEE 802.11 QoS Data
Logical-Link Control Logical-Link Control
IPv6 Header IPv6 Header
“802.11 Data” - The value of the field "Type/Subtype" in the “802.11 Data” header is 0x0020.
“802.11 QoS Data” – The value of the field "Type/Subtype" in the “802.11 QoS” header is 0x0028.
Suggestions:
Keep only “802.11 Data” Headers?
Keep both “802.11 Data” and “802.11 QoS Data”?
(in this case the Traffic Class, Flow Label and other IPv6 fields in the
diffserv context apply here as well; draft-ietf-tsvwg-ieee-802-11-00
“guidelines for DiffServ to 802.11 mapping”)

## Slide 9: Issues (4)
IP handover performance: need analysis of OCB link crowding with too frequent RAs (needed to improve IP handover performance)

## Slide 10: Issues (5)
Multicast worries in 802.11 are even more relevant in OCB mode.
  Refer to draft-perkins-intarea-multicast-ieee802-01?

## Slide 11: Solved issues – MTU (6)
Default MTU is 1500 bytes, as in IPv6-over-Ethernet (RFC2464)
Minimum MTU is 1280bytes (because 1024byte payload and 256byte headers)
To do: remove redundant text

## Slide 12: Solved Issues – MTU (6, continued)
  Non-IP packets, such as geonet have an MTU of 1492bytes, and WSMP have containers (no limits)

## Slide 13: Solved issues – Address Mapping – Multicast (7)
0x3333 is the value of the first two octets of the MAC address
  0x3333 is not listed at IEEE, yet it’s widely used
  Remove redundant text
Section 6.4.2. Address Mapping – Multicast is a restatement of RFC 2464 section 7
  remove restatement text.
Remove text about “all-yellow-taxis-in-street” – it is the definition of a multicast group

## Slide 14: Solved Issues (8)
IEEE about to make a protocol change to “LLC”, and we talk in our draft extensively about “LLC Header” (stacks, adaptation layer, etc.)
“There are two LLC sublayer protocols used (see IEEE Std 802-2014 (Overview and Architecture)): LLC Protocol Discrimination (LPD) (see ISO/IEC 8802-2:1998) and EtherType Protocol Discrimination (EPD) (see IEEE Std 802.3-2012). LPD is used for transmission of all IEEE Std 802.11 MSDUs with the exception of the 5.9 GHz bands where EPD is used (see E.2.3 (5.9 GHz band in the United States (5.850–5.925 GHz)) and E.2.4 (5.9 GHz band in Europe (5.855–5.925 GHz))). When LPD is used, …”
Suggestion:
  refer the origin of 802.11 OCB (from 802.11p-2010) only once, and never mention "802.11p" again.
  insert "in the next release of 802.11 standard, the LLC is based on 802-2014“
    Suggest the Wireshark implementer to talk about LPD and EPD as kinds of LLC.

## Slide 15: Solved Issues – Interface ID (9)
  Get rid of text in 6.5, and refer to RFC4862 and RFC7721 “Security and Privacy Considerations for IPv6 Address Generation Mechanisms”.
  Refer also to the ‘U/G’ bits RFC.
  Align with draft-ietf-6man-default-iids

## Slide 16: Solved Issues (10)
In section 5.5. Authentication requirements, there is a request that “IPv6 over 802.11-OCB packets must contain a certificate.”
  clarify the text and explain that this is a requirement to the layer above IPv6.
MAC address change:
  1) We must change our MAC address, and the embedded version in the IPv6 (and IPv4) address, and in general also any Application ID (or layer ID) that could breach privacy
  2) We are not in control on when changing our MAC address. If IEEE WAVE (BSM being sent) is running in parallel, then it should be IEEE WAVE triggering their pseudonym change AND ours.
  Sounds like an issue to be put outside the document

## Slide 17: Solved Issues (11)
Section 6.6. Subnet Structure:
  replace the text “The 802.11p networks, much like other 802.11 networks,” by a simpler “The 802.11p networks in OCB mode.”
  refer to RFC5889 “addressing model for ad-hoc networks”, draft-baccelli-multi-hop-wireless-communication-06

## Slide 18: Solved Issues (12)
Appendix D “Use of IPv6-over-802.11-OCB for distribution of certificates” – is not in scope of this document
  Remove text