## Slide 1: Generalized Routing ISCD Switching Capability Specific Information draft-ceccarelli-teas-gneralized-scsi-00
Daniele Ceccarelli daniele.ceccarelli@ericsson.com
Lou Berger lberger@labn.com

## Slide 2: Why this ID?
Issues with a CCAMP draft: draft-ietf-ccamp-ospf-availability-extension-08
  Definition of ISCD Availability sub-TLV
  Aim to use it in the SCSI of the ISCD

## Slide 3: Problems
The SCSI of the ISCD is tightly connected to the Switching Capability:
  Some examples:
    Switching Cap = 1 (Packet-Switch Capable-1 (PSC-1))
    Switching Cap = 100 (Time-Division-Multiplex Capable (TDM))
  There is no generalized way to have multiple sub-TLVs in the SCSI
    Switching Cap = 1 (PSC-1)
    Switching Cap = 100 (TDM)

## Slide 4: Solutions
Possible solution without this draft:
  Make the availability sub-TLV the SCSI for each (new) switch cap
    E.g. we define the “foo” switch cap with support for availability sub tlv
  …or duplicate all the new switch caps (1 with the availability sub-TLV supported and 1 without
  No backward utilization of the sub-TLV as for already defined Switch caps there is no room for using TLVs in the SCSI.
Solution proposed by this draft
  Define a generalized SCSI format
    Composed by zero or more sub-TLVs called SCSI TLV
    Define a new registry "Generalized SCSI (Switching Capability Specific Information) TLVs Types
    Define the availability sub-TLV as one of these TLVs (in draft-ietf-ccamp-ospf-availability-extension-08
  No backward utilization: only the newly defined switch caps referencing this document would allows for using the Generalized SCSI TLVs

## Slide 5: Open items
Value split between specific technology and others?
  New allocation requests to this registry SHALL indicate the value or values to be used in the SwitchCap column
Value | SCSI-TLV | SwitchCap | Reference
0 | Reserved |  | [This ID]
1-32768 | Unassigned, for use by specific technology | [per value] | [This ID]
32768-65535 | Unassigned, for others | Any, or value list | [This ID]

## Slide 6: Next Steps
Move quickly as stopper for a post-WG LC document
Comments?