## Slide 1: Extensions to Resource Reservation Protocol For Fast Reroute of Traffic Engineering GMPLS LSPs draft-ietf-teas-gmpls-lsp-fastreroute-06
Authors:
  Mike Taillon (mtaillon@cisco.com)
  Tarek Saad (tsaad@cisco.com)
  Rakesh Gandhi (rgandhi@cisco.com) - Presenter
  Zafar Ali (zali@cisco.com)
Contributors:
Frederic Jounay (frederic.jounay@salt.ch)
Manav Bhatia (manav.bhatia@nokia.com)
Lizhong Jin (lizho.jin@gmail.com)
97th IETF, TEAS WG, Seoul (November 2016)

## Slide 2: Outline
Scope and Current Status
Summary of Signaling Extensions
Recent Updates
Next Steps

## Slide 3: Scope and Current Status
Scope:
  Bidirectional Tunnel Signaled using GMPLS [RFC3473]
  Packet Switch Capable (PSC)
  Using FRR procedures [RFC4090]
Current Status:
  Completed WG LC
  Addressed Review comments
Presenting the recent updates in this draft as a result of the WG LC review.

## Slide 4: Summary of Signaling Extensions
Need to obtain upstream MP label and upstream MP address.
  Upstream PLR obtains the upstream MP label and upstream MP address from the RRO of the RSVP Path message.
The upstream and downstream PLRs may independently assign different FRR bypass tunnels in the forward and reverse directions.
  Co-ordinate FRR bypass tunnel selections between downstream and upstream PLRs using new Bypass Assignment RRO subobject.
After FRR activation, upstream PLR may timeout RSVP soft-state with in-band signaling when using NNHOP Bypass tunnel.
  Point of Remote Repair (PRR) reroutes Resv and traffic over the FRR bypass tunnel in the reverse direction.

## Slide 5: Upstream MP Label and MP Address
Upstream PLR obtains the upstream MP label and upstream MP address from the RRO in the RSVP Path message.
Bypass GMPLS tunnel in the same direction as the protected GMPLS tunnel (in terms of Active/Passive sides).
Active/Head
Passive/Tail
Path
Path
Path
Resv
Resv
Downstream PLR
Upstream MP
C
D
Upstream PLR
Downstream MP
Point of Remote Repair (PRR)
E
B
A
F
Resv
Bypass Tc
Resv
Path
Resv
Path

## Slide 6: Bypass Assignment Co-ordination
New Bypass Assignment (BA) subobject in RRO identifies the bypass tunnel assigned by downstream PLRs:
Bypass Assignment subobject = Bypass Tunnel ID, Bypass Destination Address
Bypass tunnel Source Address is added in Node-ID subobject in RRO [RFC4561].
New BA subobject is added after the Node-ID subobject in RRO, every time downstream PLR updates the bypass tunnel assignment.
Upstream PLR uses the recorded bypass tunnel to reflect the assignment.
Active/Head
Passive/Tail
Path
Path
Path
Resv
Resv
Downstream PLR
C
D
Upstream PLR
E
B
A
F
Resv
Resv
Path
Resv
Path
Bypass Tc

## Slide 7: Multiple Bypass Tunnel Assignments
Upstream PLR may receive multiple bypass tunnel assignments from different downstream PLRs.
  This gets corrected during re-coroute phase after Fast Reroute.
NOTIFY Message sent by the upstream PLR (Node F) to indicate the “bypass assignment can not be used” (preferring node or link protection, based on the local policy).
Allows downstream PLR to potentially change the bypass assignment before Fast Reroute event.
Active/Head
Passive/Tail
Path
Path
Path
Resv
Resv
Downstream PLR
C
D
Upstream PLR
E
B
A
F
Resv
Bypass Td
Resv
Path
Resv
Path
Bypass Te
Downstream PLR

## Slide 8: Bypass Assignment Error Notification
NOTIFY Message (Type 21, RFC3473) sent from upstream PLR to downstream PLR to notify the bypass assignment error.
NOTIFY Message contains ERROR_SPEC Object (Type 6) (with new Error-code for Bypass Assignment Error).
Sub-codes are:
  Bypass assignment can not be used
  Bypass tunnel not found
  One-to-one bypass tunnel already in-use

## Slide 9: Some Other Updates
Added terminology for Downstream and Upstream MP
Added more details on Revertive behavior after Fast Reroute
Created a section on Unidirectional Link Failures and moved relevant text there
Clarified one-to-one backup method using DETOUR object
Misc. editorial changes

## Slide 10: Next Steps
No open issues at the moment
Requesting feedback from the WG on the updates
Request for publication

## Slide 11
Thank You.

## Slide 12: FRR Reroute Phase (NNHOP bypass)
Active/Head
Passive/Tail
Path
Path
Path
Resv
Resv
Traffic + Path
Traffic
downstream PLR
C
D
Link Failure
FRR reroute phase
The downstream PLR C and upstream PLR D independently trigger fast reroute procedures to redirect traffic onto respective bypass tunnels.
The downstream PLR C reroutes RSVP Path state onto the bypass tunnel Tc [RFC4090].
At this point, node D stops receiving RSVP Path refreshes for the protected tunnel.
This eventually leads to Path state timeout for the protected tunnel.
Resv
upstream PLR
downstream MP
E
B
A
F
Resv
Bypass Tc
Bypass Tb

## Slide 13: FRR Re-coroute Phase (NNHOP bypass)
Active/Head
Passive/Tail
Path
Path
Path
Resv
Resv
Path
Resv
downstream PLR
C
D
Link Failure
FRR active state – Re-coroute Phase
E
B
A
F
Once the traffic is fast rerouted, need a way to get the protected tunnel co-routed in both directions to avoid timeouts.
Downstream MP node E assumes the role of Point of Remote Repair (PRR) (upon receiving Path message over bypass tunnel Tc).
Node E reroutes traffic in the reverse direction and Resv onto bypass tunnel Tc.
Resv
Bypass Tc
downstream MP
point of remote repair (PRR)