## Slide 1: YANG Data Models for TE and RSVP draft-ietf-teas-yang-rsvp-06 draft-ietf-teas-yang-te-05 https://github.com/ietf-mpls-yang/te
Tarek Saad and Rakesh Gandhi (Presenter), Cisco Systems
Vishnu Pavan Beeram, Juniper Networks
Xufeng Liu, Ericsson
Himanshu Shah, Ciena
Igor Bryskin, Huawei
Xia Chen, Huawei
Raqib Jones, Brocade
Bin Wen, Comcast
IETF-97, Nov 2016, Seoul

## Slide 2: Agenda
Updates (since IETF96)
Open issues
Next steps

## Slide 3: Since IETF96 Update:
Addressed compilation issues due to dependency on IETF routing model related changes:
  Example:
Draft has been stable since IET95
<draft-ietf-teas-yang-rsvp-06>

## Slide 4: Since IETF96 Update # 1 Miscellaneous Changes
Fixed data-type typo: admin-group binary length to 4-octets
Separated P2MP and P2P TE tunnels (key has name only)
Addressed compilation issues due to dependency on IETF routing model
<draft-ietf-teas-yang-te-05>

## Slide 5: Since IETF96 Update # 2 Path Constraints
Added new path metric-type (metric-hop and hop-limit)
Defined optimization criteria:
  Min-hop (metric-hop)
  Min-latency (metric-te)
  shortest (metric-igp)
RFC5541 defines more elaborate OFs and metric-types
  TBD on adding in base or extension model
<draft-ietf-teas-yang-te-05>
Notes: TE does not have extended TE model. RSVP has base and extended.

## Slide 6: Since IETF96 Update # 3 Compute-only Tunnel
Client provisions a compute-only tunnel with:
  set of paths with preferences
  per-path or per-tunnel constraints
  enables compute-only on per-path
Server computes the path(s):
  creates a state (LSP) per path
  state of computed path and changes there-on are reflected in the LSP(s)
  no resources are committed/reserved
  no signaling
Client notified of computed path(s):
  polling the server
  subscribe/publish on the compute-only tunnel
Re-computation of paths:
  periodic or topology event driven
<draft-ietf-teas-yang-te-05>

## Slide 7: Since IETF96 Update # 4 Model RPCs
Requirement: support to post actions on model objects (e.g. tunnels, links)
YANG 1.1 allows posting action (RPC) support on per object
Defined new actions on TE tunnels:
  re-setup
  re-optimize
  switch-path
  compute-path
    Result may not be returned immediately
    Need to asynchronously return result
Returned result:
  immediate: success, fail or in-progress
<draft-ietf-teas-yang-te-05>
Notes: For in-progress, can register via pub/sub or poll object e.g. state up/down or new-lsp-id.

## Slide 8: Open Issue # 1 Reuse of TE model for different technologies (Revisit from IETF96)
OPTION # 1: defines reusable groupings (tunnels, LSPs, etc.) in generic module(s) that technology models reuse
OPTION # 2: technology models make use of schema mount to load TE generic model for different technologies
OPTION # 3 (current state of model): TE generic model defined at the root/TOP of tree with per data node technology type
<draft-ietf-teas-yang-te-05>

## Slide 9: Open Issue # 2 Telemetry/counters/stats
Complete definition of supported counters/stats
Subset that all vendors support with use of if-features?
<draft-ietf-teas-yang-te-05>

## Slide 10: Open Issue # 3 Bandwidth Type: Generic vs. per technology
  Discussion on using generic BW type in TE technology agnostic models
    String with no strict type check
    Interpreted based on the specific technology
    For example:
      For packet, a float number format that uses IEEE floating-point may be used, such as “0x1p10”
      For OTN, a list of CSV integers may be used, such as “0,2,3,1”, e.g. ODU units
  Currently, technology specific module(s) use distinct type per technology, e.g.
    BW for packet LSP use integer for “bps”
  The two need to be mutually exclusive
<draft-ietf-teas-yang-te-05>

## Slide 11: Next Steps
Conclude on open issues
Request further review and address comments
Complete the augmentation for module:
  PCC-TE data

## Slide 12
Thank You

## Slide 13: TE/RSVP and MPLS YANG Modules Structure and Relationship
ietf-te-device.yang
ietf-te-rsvp.yang
ietf-rsvp.yang
ietf-te-sr-mpls.yang
ietf-te-rsvp-mpls.yang
augment
To be defined
YANG module
Defined
YANG module
ietf-mpls-base.yang
ietf-rsvp-ext.yang
ietf-te.yang
mount ?
ietf-te-pcc.yang
ietf-otn-base.yang

## Slide 14: Summary Open Issue #1
Option | Reusability of Generic Data | Dependency between data nodes (leafref) | Separation of technology specific data | Augment of generic model
OPTION #1 (groupings) | ✓ | ✗ | ✓ | Only when grouping is used
OPTION #2 (mount) | ✓ | Not outside mount space | ✓ | ✓
OPTION #3 (multi-technology generic model) | ✓ | ✓ | ✗ | ✓