## Slide 1: Abstraction and Control of TE Networks (ACTN) Abstraction Methods
draft-lee-teas-actn-abstraction-00
IETF 97 – Seoul
Young Lee (Huawei)
Dhruv Dhody (Huawei)
Oscar Gonzalez de Dios (Telefonica)
Daniele Ceccarelli (Ericsson)

## Slide 2: Abstraction
Abstraction is defined in [RFC7626] as:
Abstraction is the process of applying policy to the available TE information within a domain, to produce selective information that represents the potential ability to connect across the domain. Thus, abstraction does not necessarily offer all possible connectivity options, but presents a general view of potential connectivity according to the policies that determine how the domain's administrator wants to allow the domain resources to be used.

## Slide 3: Factors impacting the abstraction
Nature of the underlying domain
  Packet vs Transport
PNC capabilities
  Route reflector
  Abstraction algorithms
  Computation request/reply
MDSC capabilities
  Ditto
Scalability and Frequency of updates
  Trade-off between scalability and level of details
PNC
PNC
MDSC
CNC
Y
Abstraction
Abstraction + VN

## Slide 4: Abstraction level
Topology Abstraction Level
No abstraction: Native topo/ White
Total abstraction: Abstract node/Black
Shades of grey

## Slide 5: White topology (Native)
Topology Abstraction Level
No abstraction: Native topo/ White
The PNC:
  …provides the actual network topology to the MDSC without any hiding or filtering.
The MDSC:
  …has the full knowledge of the underlying network topology and as such there is no need for the MDSC to send a path computation request to the PNC. The computation burden will fall on the MDSC.

## Slide 6: Black topology (Abstract node)
Topology Abstraction Level
Total abstraction: Abstract node/Black
With border nodes
Total abstraction: Abstract node/Black
Without border nodes
MDSC- PNCs interaction needed for end2end path computation
Small amount of info exchanged between PNC and MDSC but high interaction

## Slide 7: Grey topology
Grey topology type A:
border nodes with a TE links between them in a full mesh fashion
Grey topology type B:
border nodes with some internal abstracted nodes and abstracted links
Shades of grey
Topology Abstraction Level
Types
Automatic generation of abstract topology by configuration
On demand of supplementary topology via path computation request/reply
How to build it

## Slide 8: Requirements for capability negotiation for abstraction level
It is expected that the abstraction level be negotiated between the CNC and the MDSC (i.e., the CMI) depending on the capability of the CNC.
This negotiated level of abstraction on the CMI may also impact the way the MDSC and the PNCs configure and encode the abstracted topology.
  For example, if the CNC is capable of sophisticated technology specific operation, then this would impact the level of abstraction at the MDSC with the PNCs.
  On the other hand, if the CNC asks for a generic topology abstraction, then the level of abstraction at the MDSC with the PNCs can be less technology specific than the former case.

## Slide 9: Requirements for Abstraction type definition and its parameters
Packet Networks: For grey abstraction, the type of abstraction and its parameters MUST be defined and configured/negotiated.
Abstraction Level 1: TE-tunnel abstraction for all (S-D) border pairs with:
  Maximum B/W available per Priority Level
  Minimum Latency
OTN Networks: For grey abstraction, the type of abstraction and its parameters MUST be defined and configured/negotiated.
Abstraction Level 1: Per ODU Switching level (i.e., ODU type and number) TE-tunnel abstraction for all (S-D) border pair with:
  Maximum B/W available per Priority Level
  Minimum Latency
Abstraction Level 2: Aggregated TE-tunnel abstraction for all (S-D) border pairs with:
  Maximum B/W available per Priority Level
  Minimum Latency
WSON Networks: For grey abstraction, the type of abstraction MUST and its parameters be defined and configured/negotiated.
Abstraction Level 1: Per Lambda/Frequency level TE-tunnel abstraction for all (S-D) border pairs with:
  Maximum B/W available per Priority Level
  Minimum Latency
Abstraction Level 2: Aggregated TE-tunnel abstraction for all (S-D) border pairs with:
  Maximum B/W available per Priority Level
  Minimum Latency

## Slide 10: Next Steps
This I-D discusses all the issues around abstraction:
–Factors that affect abstraction
–Abstraction methods
–How to build topology
–Requirements that may impact data model/protocol design
Any other missing issues around abstraction?
Is this useful?