## Slide 1
Young Lee (Huawei)
Sergio Belotti (Alcatel-Lucent)
Daniele Ceccarelli (Ericsson)
Dhruv Dhody (Huawei)
Bin Young Yun (ETRI)
draft-leebelotti-teas-actn-info-05
IETF 97 – Seoul
ACTN Information Model

## Slide 2: Updates from 04 version
Terminology alignment and refinement
  among this draft and companion ACTN WG drafts (Requirements and Framework)
  With RFC 7926 [Interconnected-TE]
Major effort on object refinement. Also added
  VN Objective Function
  VN Computed Path list
Refinement on mapping between primitives and objects.
Attention is given to compatibility with other information model proposed in the context of other SDOs.

## Slide 3: Action Primitives (no update)
VN Action | Description
VN Instantiate | Customer/application (C/A) requires their VNs (1)
VN Modify | C/A request for modification of a VN (1)
VN Delete | C/A request to delete a VN (1)
VN Path Compute | C/A request for a priory exploration to estimate network resource availability before making a VN instantiate decision (1) (2)
VN Query | Permit to get topology view (pull model)
VN Update | Refers to any update to the VN that need to be reported to the subscribers (push model)
TE Update | TE update from any PNC to MSDC (complete or abstracted filtered view of TEDB)
(1) This primitive can also be applied from the MDSC to a PNC requesting a VN (if the PNC can instantiate the entire VN or a part of VN)
(2) This action is necessary from the MDSC to PNCs to determine the end-to-end multi-domain path, in this case a double-stage Path Computation takes place, first on the abstracted end-to-end network view (happening at CNC-MDSC ), and on the second stage it shall be expanded by each PNC.

## Slide 4: Objects (1)
Objects | Description
VN Identifier | Unique VN identifier
VN Service Characteristics | Type of VN connectivity (P2P/P2MP..etc),Traffic matrix parameter (BW + VN Constraints), Survivability (VN recovery level)
VN Objective Function | The VN Objective Function applies to each VN member (i.e., each E2E tunnel) of a VN. Referred to objective functions defined in RFC 5541 (MCP,MLP etc)
VN End-Point | VN’s customer end point characteristics : Access Point Identifier, Access Link Capability, Source Indicator
VN Action status | Result of a VN action
VN Associate LSP | Describes the instantiated LSPs that is associated with the VN.
VN Computed Path | List of paths obtained after the VN path computation request from a higher controller.
VN Service Preference | It refers to (a) End Point Location’s support for certain VNF (security, firewall), (b) client-specific preference enforcement to permit correct selection from the network of the destination related at the indicated VNF, (c) End-Point Dynamic Selection Preference if end point can support e.g. (disaster recovery or VM migration) and so can be part of the selection by MDSC following (b))

## Slide 5: Mapping of Primitives with Objects
<VN Instantiate> ::= [<VN Service Characteristics>]
<VN End-Point>
<VN Objective Function>
[<VN Service Preference>]
<VN Modify> ::= <VN identifier>
<VN Service Characteristics >
[<VN Objective Function>]
<VN End-Point>
[<VN Service Preference>]
<VN Delete> ::= <VN Identifier>
<VN Update> :: = <VN Identifier>
<VN Associated LSP>
<VN Path Compute Request> ::=::= <VN Service Characteristics>
<VN End-Point>
<VN Objective Function>
<VN Path Compute Reply> ::= <VN Computed Path>
<VN Query> ::= <VN Identifier>
<VN Query Reply> ::= <VN Identifier>
<VN Associated LSP>

## Slide 6: Next Steps
Co-authors believe that the draft is ready for WG adoption
Exploiting this information model - work has started on solution drafts. E.g.,
  ACTN VN Yang Model for CMI: draft-lee-teas-actn-vn-yang-02
  PCE Applicability for ACTN: draft-dhody-pce-applicability-actn-01

## Slide 7
BACKUP

## Slide 8: ACTN Model background
The model is described in terms of
  Action Primitives : they are basic actions needed to support different ACTN network control functions e.g. network topology request/query , VN service instantiation/deletion/modifications, path computation, VN service policy negotiation/enforcement
  Objects and their properties (attributes) : the object represents ACTN resources needed to be exchanged along interfaces and used in the context of primitives.

## Slide 9: VN Definition
A Virtual Network is a client view (typically a network slice) of the transport network. It is presented by the provider as a set of physical and/or abstracted resources. Depending on the agreement between client and provider various VN operations and VN views are possible. There are three aspects related to VN:
VN Creation: VN could be pre-configured and created via static negotiation between customer and provider. In other cases, VN could also be created dynamically based on the request from the customer with given SLA attributes which satisfy the customer's objectives.
Dynamic Operations: VN could be further modified and deleted based on customer request to request changes in the network resources reserved for the customer. The customer can further act upon the virtual network resources to perform E2E tunnel management (set-up/release/modify). These changes will incur subsequent LSP management on the operator's level.
VN View: (a) VN can be seen as an (or set of) e2e tunnel(s) from a customer point of view where an e2e tunnel is referred as a VN member. Each VN member (i.e.,e2e tunnel) can then be formed by recursive aggregation of lower level paths at a provider level. Such end to end tunnels may comprise of customer end points, access links, intra domain paths and inter-domain link. In this view VN is thus a list of VN members. (b) VN can also be seen as a terms of topology comprising of physical and abstracted nodes and links. The nodes in this case include physical customer end points, border nodes, and internal nodes as well as abstracted nodes. Similarly the links includes physical access, inter-domain and intra-domain links as well as abstracted links. The abstracted nodes and links in this view can be pre-negotiated or created dynamically.

## Slide 10: Virtual Network
EP 1.a
EP 2.a
EP 3.a