## Slide 1: Recommendations for RSVP-TE and Segment Routing LSP co-existence draft-sitaraman-sr-rsvp-coexistence-rec-01
Harish Sitaraman (Juniper Networks)
Vishnu Pavan Beeram (Juniper Networks)
Ina Minei (Google, Inc)
Siva Sivabalan (Cisco)
draft-sitaraman-sr-rsvp-coexistence-rec-01

## Slide 2: Motivation
Placement of SR LSPs in the same domain as RSVP-TE LSPs MUST NOT introduce inaccuracies in the TED that is used by distributed or centralized RSVP Path computation engines.
  Generic problem associated with management of dark bandwidth pools.
Draft discusses various solution options for keeping the traffic engineering database (TED) consistent across the network, accounting for the different bandwidth utilization between SR and RSVP-TE.
draft-sitaraman-sr-rsvp-coexistence-rec-01

## Slide 3: Solution Options
Static Partitioning of Bandwidth
  Static reservable bandwidth of an interface is statically partitioned between SR and RSVP-TE and each can operate within that bandwidth allocation.
  Drawback:
    Inability to use the reservable bandwidth effectively; inability to use bandwidth left unused by the other protocol.
Centralized Management of Available Capacity
  Central controller performs path placement for both RSVP-TE and SR LSPs.
  Drawback:
    Requires the introduction of a central controller managing the RSVP-TE LSPs as a prerequisite to the deployment of any SR LSPs.
draft-sitaraman-sr-rsvp-coexistence-rec-01

## Slide 4: Solution Options (Cont..)
Flooding SR Utilization in IGP
  SR utilization information can be flooded in IGP-TE and the RSVP-TE path computation engine (CSPF) can be changed to consider this information.
  Drawback:
    Requires changes to the RSVP-TE path computation logic ; Requires upgrades in deployments where distributed computation is done across the network.
Running SR over RSVP-TE
  SR can run over dedicated RSVP-TE LSPs that carry only SR traffic.
  Drawback:
    Requires SR to rely on RSVP- TE for deployment.
draft-sitaraman-sr-rsvp-coexistence-rec-01

## Slide 5: Solution Options (Cont..)
TED consistency by reflecting SR traffic (adjusting Max-Reservable-BW)
  Dynamically measure SR traffic utilization on each TE interface and reduce the bandwidth allowed for use by RSVP-TE.
    No change to computation logic on RSVP Path Computation engines.
  Procedure - On each TE-Node logic:
    Periodically, retrieve SR traffic statistics for each TE interface.
    Periodically, calculate SR traffic average over a set of collected traffic samples.
    If the change in SR traffic average is greater than or equal to SR traffic threshold percentage (configured), then adjust the Max-Reservable-BW.
      This would result in the RSVP-Unreserved-BW-At-Priority-X getting adjusted.
draft-sitaraman-sr-rsvp-coexistence-rec-01

## Slide 6: Next Steps
draft-sitaraman-sr-rsvp-coexistence-rec-01
Request WG review/feedback.