## Slide 1
PCECC Use cases update
draft-zhao-teas-pcecc-use-cases-03
Boris Khasanov (Huawei)
Andrey Elperin (Kyivstar)

## Slide 2
In updated version of the draft we covered the comments that were given during TEAS-96 WG session (we addressed comments from Dieter and others).
Together with Aijun Wang we decided to divide work on PCE in native IP network as separate draft (draft-wang-teas-pce-native-ip)
We added one new customer use case (Inter-AS TE will be presented below)
New version was published
Current status

## Slide 3
The Use Cases for Using PCE as the Central Controller (PCECC) of LSPs:
PCECC and Inter-AS TE

## Slide 4
Kyivstar network overview
Kyivstar is the largest mobile operator (more than 26M subs) and the second largest fixed broadband provider (0.9M subs) in Ukraine
Full set of services for B2B subscribers: mobile services, FMC, L2/L3 VPNs, IP transit and so on
The largest mobile broadband coverage in Ukraine
IP/MPLS enabled POPs in more than 100 cities all over Ukraine (more cities will be available soon)
We are operating our IP/MPLS networks in Inter-AS environment because after acquisition of one
our competitors in 2012, some parts of his network are still functioning separately

## Slide 5
L2 VPNs implementation without PCECC
L2 VPN services are VERY popular in Ukraine
To be able to provide L2 VPN services in Inter-AS environment there are some NNIs between our primary and secondary ASes
Totally we have 9 geographically distributed NNIs and several thousands of L2 Inter-AS VPNs
There are two types of Inter-AS L2 VPNs – intra-city and inter-city
One of the main customer demands for intra-city VPNs is to minimize RTT and to provide protection for the service
Taking into account geographical distribution of NNIs it’s quite complicated for us to fulfill this requirements using legacy Inter-AS L2 VPNs option B.

## Slide 6
PCECC implementation of Inter-AS transport LSP for L2VPN
PCECC should establish control plane (BGP-LS and PCEP) connectivity with routers (BGP-LS could be only with RRs) in both domains
PCC and PCECC exchange PC Open messages with PCECC capability
PCECC calculates primary and backup transport TEs following given constrains (i.e. minimal delay for primary, path diversity for the backup)
PCECC add those LSPs and download labels to the routers (PCCs) along the path in both domains via PCEP (PCLabelUpd)
PCECC updates LSP, router starts to use it as Inter-AS transport LSP

## Slide 7
LSPs after centralized path computation
After LSPs calculation and provisioning by PCECC, we will have E2E MPLS-enabled Inter-AS transport for L2VPN services
L2VPN traffic will flow by optimal path. In case of primary LSP failure, traffic will switch to backup LSP. A lot of different constrains may be considered during backup LSP path calculation

## Slide 8
Next steps
We think that draft is stable and could be considered for WG adoption poll

## Slide 9
Thank you!