## Slide 1: Multi-stream Media Conferencing
Bo Burman
Ericsson AB
draft-westerlund-clue-multistream-conference-00

## Slide 2: Purpose
The draft defines a framework and requirements for allowing endpoints with different capabilities to participate in a conference, with each endpoint being able to use as high-quality media as possible

## Slide 3: Overview
A set of selected use cases
  Each focusing on an end-point category
  Tries to avoid transcoding
Proposed methods to support the above
  RTP usage
  Signaling extensions

## Slide 4: Assumptions
End-points of different “quality categories” are present in the same conference
It is desirable to use as high quality media as possible to every end-point
A more capable, higher quality, end-point can always receive a lower quality stream encoded with the same codec

## Slide 5: Low Quality Sender
Low
Med
High
Dual High
RTP
Mixer
Low
?

## Slide 6: Medium Quality Sender
Med
High
Dual High
RTP
Mixer
Low
?
Med

## Slide 7: Medium Quality Sender
Med
High
Dual High
RTP
Mixer
Low
?
Med
T
Transcoding

## Slide 8: Medium Quality Sender
Med
High
Dual High
RTP
Mixer
Low
?
Med
Simulcast
draft-westerlund-avtcore-rtp-simulcast

## Slide 9: Medium Quality Sender
Med
High
Dual High
RTP
Mixer
Low
?
Med
Scalable coding

## Slide 10: Dual Channel Sender
Med
High
Dual High
RTP
Mixer
Low
Dual High
?
?
?
Same concerns and alternative solutions for different qualities as described above
apply for each channel
Possible choice “policies”:
Active speaker
Compose 21 in Mixer
Receiving user chooses
…
Dual High
RTP
Mixer
High
Dual High
RTP
Mixer
Med
High
Dual High
RTP
Mixer
Low
Med
High
Dual High
RTP
Mixer
Dual High
Low
Med
High
Dual High
RTP
Mixer

## Slide 11: Multiple Channel Sender
Low
Med
High
Dual High
RTP
Mixer
Multiple High
How many channels could and should be sent?
max-recv-ssrc=“many”
max-send-ssrc=4
max-send-ssrc=“many”
draft-westerlund-avtcore-max-ssrc-00
max-recv-ssrc=2
max-recv-ssrc=1
max-recv-ssrc=1
max-recv-ssrc=1
An answerer’s max-send-ssrc ≤ offerer’s max-recv-ssrc

## Slide 12: Multi-quality Local Composition
RTP
Mixer
Assuming RTP Mixer has a choice of qualities available
*: max-send-ssrc=“many”
draft-westerlund-avtcore-max-ssrc-00
High: max-recv-ssrc=1 Med: max-recv-ssrc=1 Low: max-recv-ssrc=3
High
Low
Med
Low
Low

## Slide 13: Mixer Stream Roles and SSRC
RTP
Mixer
Mixer SSRC has a “role” and the source that currently holds that “role” is identified by CSRC
Active speaker
Quiet
Last
Quiet
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (B)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (D)
SSRC M3 (A) SSRC M4 (C) SSRC M5 (E)
Mixer SSRC need not change often and should be feasible to tie to a certain decoder resource

## Slide 14: Mixer Stream Roles and SSRC
RTP
Mixer
Mixer SSRC has a “role” and the source that currently holds that “role” is identified by CSRC
Active speaker
Quiet
Last
Quiet
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (A)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B)
SSRC M3 (D) SSRC M4 (C) SSRC M5 (E)
Mixer SSRC need not change often and should be feasible to tie to a certain decoder resource

## Slide 15: Mixer Stream Roles and SSRC
RTP
Mixer
Mixer SSRC has a “role” and the source that currently holds that “role” is identified by CSRC
Active speaker
Quiet
Last
Quiet
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (A)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B, D, C, E)
Some Mixer SSRC may be “composed” by the Mixer and contain multiple CSRC

## Slide 16: Receiver Stream Selection
RTP
Mixer
Receiving end-point wants to tie a certain source SSRC to a certain Mixer SSRC (and thus role)
Active speaker
Quiet
Last
Quiet
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (A)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B)
SSRC M3 (D) SSRC M4 (C) SSRC M5 (E)
“Give me D in M1”
draft-westerlund-dispatch-stream-selection-00

## Slide 17: Receiver Stream Selection
RTP
Mixer
Receiving end-point wants to tie a certain source SSRC to a certain Mixer SSRC (and thus overrides “role”)
Quiet
Quiet
Last
Active
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (D)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B)
SSRC M3 (A) SSRC M4 (C) SSRC M5 (E)
“Ack”
draft-westerlund-dispatch-stream-selection-00
Quiet
What to do with replaced “roles” is subject to Mixer implementation and policy; for further consideration

## Slide 18: Avoid Unused Streams
RTP
Mixer
Mixer notices that C and E streams are currently not received by anyone and decides to pause them
Active speaker
Last
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (A)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B)
SSRC M3 (D)
draft-westerlund-avtext-rtp-stream-pause-00
“Pause C”
“Pause E”

## Slide 19: Avoid Unused Streams
RTP
Mixer
C and E streams are paused and the pauses are ack’ed
Active speaker
Last
Quiet
Active speaker
Last active speaker
Quiet
Quiet
Quiet
SSRC A
SSRC M1 (A)
SSRC C
SSRC D
SSRC E
SSRC B
SSRC M2 (B)
SSRC M3 (D)
Paused streams must be possible to resume very quickly if they are wanted again
draft-westerlund-avtext-rtp-stream-pause-00
“Ack C”
“Ack E”

## Slide 20: Expected Outcome
CLUE is asked to take the presented use cases and proposed solutions into account in its work and when progressing the WG drafts