## Slide 1: CLUE Framework 03 – comments and issues
Interim meeting February 2012 Roni Even
Notes: <number>

## Slide 2: Major issues
Message flow
CLUE and SDP media description.
Individual encoding
Encoding groups
Other issues
Framework roadmap.

## Slide 3: Message flow
Section 9.4 specifies three messages
  Consumer capabilities
  Capture advertisement
  Configure encoding
Is there a need for three messages? Can we use just two.
  Consumer capabilities for decoding can be different from the number of monitors.
  Provider can advertise full information.
  Consumer can use part of a capture set entry based on the number of streams it wants to use.
  Providing full information will allow the consumer a better selection.
  Having two messages will work better with offer / answer model and will use less messages.
Can have the consumer capabilities as a separate optional message, not part of the message flow with some basic information. No need for all attributes.

## Slide 4: CLUE and SDP media description
CLUE media capture provides information about a media stream, e.g. left camera. There are multiple media captures in CLUE.
SDP provides information about the media stream like encoding and decoding capabilities.
Need to provide information that will map a media capture to an RTP stream.
Is there a need for an attribute in CLUE
Should this be specified in the CLUE transport work.
  There is draft-lennox-clue-rtp-usage-02 that propose part of the solution.
Submitted an initial proposal in draft-even-clue-rtp-mapping-00.
  Media description in SDP can be mapped to multiple MCs.
  Number media different media description is as the number of simultaneous MCs in a capture set entry. The mapping can be done using SDP grouping.
  Any conference mapping information for identifying participants stream can be done using the conference event package.

## Slide 5: Individual encoding
Section 7.1 defines the following variables for individual encodings:
  maxBandwidth
  maxH264Mbps
  maxWidth
  maxHeight
  Maximum supported frame rate
All these variables are specified also in SDP and some of them are codec specific.
A new codec may require new variables
Propose to map the SDP information to CLUE and nit duplicate information.
For usage see next slide on encoding groups.

## Slide 6: Encoding groups
Encoding groups are used to specify encoding constrains of an endpoint for multiple streams.
This is not a CLUE specific problem. A non CLUE use case if for Dual stream (H.239 like people and content). May have different encoding constrains if sending one or two video streams.
Variables include maxGroupBandwidth which is also specified in SDP.
Issues:
  Should this be in CLUE or a separate general functionality using SDP?
  If in CLUE, should be optional for the provider since can have no constrains.

## Slide 7: Other issues
Provider or Consumer, who decide what will be the media content. Switching / mixing offers.
What is CLUE message rate.
What is CLUE message size.