## Slide 1: RTP Usage for CLUE draft-lennox-clue-rtp-usage-02 Clue WG Interim – 16 February 2011
Jonathan Lennox jonathan@vidyo.com
Allyn Romanow allyn@cisco.com
Paul Witty paul.witty@balliol.oxon.org

## Slide 2: RTP Requirements for CLUE
CLUE permits SIP calls to have many media sources
  Easily dozens at a time, e.g. for continuous presence in multipoint sessions.
  Potentially choosing among hundreds of inputs (for switched or composited captures).
  Number of media sources can be asymmetric and dynamic.

## Slide 3: Architectural constraints
Initial offer shouldn’t confuse non-CLUE endpoints.
Signaling messages shouldn’t confuse SIP middleboxes.
Transport flow usage (for NATs, FWs, port consumption on MCUs, etc.) should be restrained and static.

## Slide 4: Source multiplexing
Send all sources of the same media type over a single RTP session.
Even though these correspond to different CLUE captures.
(Unless you need different transport treatment.)
Camera 1
Camera 2
Camera 3
Screen1
Screen 2
Screen 3

## Slide 5: Complications for CLUE
Receiver needs to interpret sources it receives, and correlate them with captures it has requested.
In some cases, CLUE Framework captures map to RTP sources (SSRC), but in many cases they do not.

## Slide 6: Use Case 1: Static Source Choice
Sources are constant over complete session
Endpoint
Endpoint

## Slide 7: Use Case 2: Point to Point Finite Sources
Choice from among a small set of sources
Set of sources might change over a session
A source might move between switched captures
Endpoint
Endpoint
L
R

## Slide 8: Use Case 2: Point to Point Finite Sources
Choice from among a small set of sources
Set of sources might change over a session
A source might move between switched captures
Endpoint
Endpoint
L
R

## Slide 9: Use Case 3: Multipoint Unbounded Sources
Switched multipoint device: MCU sends sources from any endpoint to any other, switching dynamically.
EP
EP
EP
EP
MCU

## Slide 10: Mapping sources to captures
A capture might correspond to one or more sources.
A source might be used for one or more captures.
Sources are identified by SSRC, but SSRC is a random number with no further information.

## Slide 11: Need for accurate mappings
Some equipment needs to know source-to-capture mappings before decoding.
  Dedicated decoder hardware: one-out-one-in.
  Decoder hardware associated with specific displays/speakers.
Receiving mapping information late can mean discarding packets, leading to poor switching times, excess I-Frame requests, etc.

## Slide 12: Need for flexible mappings
Conversely, some equipment can share decoder state as sources move between captures.
  E.g. continuous presence screen: 16 recent speakers.
    (Details of policy choice not important here.)
  Same source being sent for more than one capture.
Don’t want to require unnecessary I-frames or duplicate transmission.

## Slide 13: Sending mapping outside media
In CLUE messaging
  Reliable, but not time-guaranteed.
  Depending on how CLUE is sent, might be very heavyweight.
In RTCP SDES
  Unreliable; subject to RTCP timing/bandwidth rules.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| CaptureID=9 | length=4 | Capture ID :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 14: Sending capture IDs in media stream
Tag media packets with capture IDs
Advantages:
  No latency or possibility of confusion
Disadvantages:
  Processing load for switching MCU
    Capture IDs are scoped to each hop.
  Additional packet overhead: potential bandwidth or MTU issues.

## Slide 15: RTP Header Extension
Can carry capture ID in RFC 5285 header extension
  a=extmap:1 urn:ietf:params:rtp-hdrex:clue-capture-id
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ID=1 | L=3 | capture id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| capture id |
+-+-+-+-+-+-+-+-+
Modification could be costly, especially for SRTP (reauthentication required).
RTP header extensions “MUST only be used for data that can safely be ignored by the recipient” – semantics are unclear. (Need SDES as well?)
Defining this wouldn’t be in scope for CLUE anyway (presumably would be AVTEXT).

## Slide 16: When to send Capture ID
Option 1: always
  Disadvantages as mentioned
Option 2: as needed
  With I-frames, or for some period of time following a capture ID switch.
  Imposes additional state-maintenance requirements on receivers.
  May need refresh request AVPF feedback message.
Recommendation: MUST support option 1, MAY negotiate option 2.