## Slide 1: CLUE Framework
Interim Meeting Feb 15, 2012
Mark Duckworth
Allyn Romanow
Brian Baldino
Andy Pepperell

## Slide 2: Agenda
Document changes since IETF82
Framework structure
Spatial relationship
Ticket #5 and #7 – composed/switched captures
Consumer Capability Message Proposal
Voice activity
Ticket #4 – share metadata with W3C
Handling document review comments

## Slide 3: Changes since IETF82
In draft-ietf-clue-framework-02
  Spatial relationships
  Coordinate system
  Area of capture, point of capture
  Area scale
In draft-ietf-clue-framework-03
  Reorganize and clarify. More concise.
  Address some review comments

## Slide 4: Framework structure – Captures
Encoding Group N
Media Capture N
Capture Set N
Capture Set 1
Attributes
Area of Scene
Scale
Simultaneous Sets
Set1 (list of MCs)
SetN (list of MCs)
Entries
Entry1 (list of MCs)
EntryN (list of MCs)
Media Capture 1
Attributes
Area of Capture
Point of Capture
Audio Channel Format
Composed/Switched
Layout/Policies
Encoding Group ID
more . . .
Provider Advertisement
Encoding Group 1

## Slide 5: Framework Structure – Encoding Groups
Encoding Group N
Encoding Group 1
encodeGroupID
maxGroupBandwidth
maxGroupH264Mbps
Video Encodings
Encoding1 (ID, maxBandwidth, maxH264Mbps, maxWidth, maxHeight, maxFrameRate)
EncodingN (ID, maxBandwidth, maxH264Mbps, maxWidth, maxHeight, maxFrameRate)
Audio Encodings
Encoding1 (ID, maxBandwidth)
EncodingN (ID, maxBandwidth)

## Slide 6: Framework Structure Summary
Encoding Group N
Media Capture N
Capture Set N
Capture Set 1
Attributes
Simultaneous Sets
Entries
Entry1 (list of MCs)
EntryN (list of MCs)
Media Capture 1
Attributes
Encoding Group 1
parameters
Video Encodings
Encoding1 (parameters)
EncodingN (parameters)
Audio Encodings
Encoding1 (ID, maxBandwidth)
EncodingN (ID, maxBandwidth)
Provider Advertisement

## Slide 7: Spatial Relationship Coordinates
Review of what has been in the document since -02 version
Area of capture,
top left: -1000, 3000, 500
Point of capture:
10, 10, 10
Area of capture,
bottom left:
-1000, 3000, -500
Area of capture,
top right:
1000, 3000, 500
Area of capture,
bottom right:
1000, 3000, -500

## Slide 8: Spatial Relationship Example
VC0
VC1
VC2
100,0
0,0
-100,0
-50,120
150,100
Area of capture co-ordinates (x,y) (z values not show)
Point of capture co-ordinates (x,y)
(table)
-150,100
50,120
x axis
y axis

## Slide 9: Ticket #5 and #7 Composed/Switched Captures
Points for discussion:
  Attributes can be a list of alternatives; consumer can choose one
  Provider advertises <video-layouts>; consumer selects one
    mediactrl/xcon video-layout
    Stephan’s proposal (email Oct 14) using bitstream coordinates ?
  Provider advertises <switch-policies>; consumer selects one
    Active speaker, round robin, site switch, segment switch, combinations of these
  Provider advertises list of sources that go into a composed/switched source (if it is known up front)
    Stephan’s proposal (email Oct 14); Marshall’s proposal (email Jan 24)

## Slide 10: Consumer Capability Message
Proposal to add this detail to the framework
Sent from the consumer to the provider
  Must be the first message sent by the consumer
  Provider must not send CLUE messages until this is received from the consumer
In common with other CLUE messages, the consumer may sent additional updates at any time

## Slide 11: Consumer Capability cont’d
Consumer tells provider which attributes and media types it understands
Allows consumer side to be simpler and implement only the subset of features that makes sense to it
Allows forward compatibility with new features
  Provider must not advertise multiple captures which the consumer would be unable to differentiate

## Slide 12: Indicating “activity” – voice or other criteria
Authors will update a previous proposal and present it on the email list

## Slide 13: Ticket #4 – share metadata with W3C
Not ready for this yet.
Need to get more stability in the framework and some progress on mapping framework elements to a data model

## Slide 14: Other review comments
Authors will track and respond to all the document review comments on the list
If there is time, we can talk about any of the review comments here