## Slide 1: Use cases for RTP Multiplexing IETF CLUE – 15/16 Feb 2012
Gerard Fernando gerard.fernando@zteusa.com
Xiaoyang Ye ye.xiaoyang@zte.com.cn

## Slide 2: Use cases for RTP Multiplexing
Why are we addressing these in the CLUE WG?

## Slide 3: RTP Session
The key feature of an RTP Session is that each session maintains a full and separate address space for SSRC. Westerlund in [draft-westerlund-avtcore-multiplex-architecture-00] defines an RTP Session as a 5-tuple (Transport protocol, Source address, Source port, Destination address, Destination port).
Notes: <number>

## Slide 4: Transport flow
Transport flow is used to transport RTP packets; each transport flow has separate packet sequence number space.

## Slide 5: RTP Source stream
One RTP Source stream includes continuous data which can be encoded and/or decoded separately from another RTP Source stream.

## Slide 6: Source multiplexing: use case 1
No multiplexing: Each RTP session just include one media type, corresponding to one transport flow, which transmit one RTP source stream).

## Slide 7: Source multiplexing: use case 2
Multiplexing based on media type: Each RTP session includes one media type which includes multiple transport flows and each transport flow corresponding to one RTP source stream.

## Slide 8: Source multiplexing: use case 3
Multiple streams in one transport flow using the same SSRC : one transport flow with one SSRC can include multiple streams identified by extended RTP header. This is especially useful for audio in CLUE.

## Slide 9: Source multiplexing: use case 4
Multiple streams in one transport flow identified by different SSRC: one transport flow can include multiple streams with the same sequence number space and different SSRC. The receivers identify the media stream from the SSRC.

## Slide 10: Source multiplexing: use case 5
Multiplexing all media streams in a single RTP session: Just like CASE 2, but both audio and video streams are included in the same RTP session.

## Slide 11: Source multiplexing: use case 6
Hybrid model: 2 or more cases above can be used at the same time. In a single RTP session, can transmit multiple streams through different model.