## Slide 1: Analysis on Two Methods in Ingress Local Protection

## Slide 2: Contents
Introduction
Descriptions on Two Methods
Analysis on Two Methods

## Slide 3: Introduction
Important to have Ingress/Egress Local Protection
Faster than E2E global protection for ingress/egress
More Scalable since keeping less states and using less resources
Easier to operate and maintain
In Ingress Local Protection:
Relay-Message or Proxy-Ingress can be used to transfer information about ingress local protection from primary ingress to backup ingress
They are described in the following slides
Detailed analysis on them are given for your reference

## Slide 4: Contents
Introduction
Descriptions on Two Methods
  Changes for Relay-Message vs. Proxy-Ingress
  Relay-Message with Example
  Proxy-Ingress with Example
Analysis on Two Methods

## Slide 5: Changes for Relay-Message vs. Proxy-Ingress
Changes for Relay-Message | Changes for Proxy-Ingress
1) Primary ingress sends Path messages with Ingress-Protection object to backup ingress after the primary LSP is set up. | 1) Primary ingress handles the configuration of proxy-ingress or generates the information for the proxy-ingress and makes sure that the proxy-ingress address generated does not cause a loop.
2) Backup ingress creates backup LSP to locally protect the primary ingress after receiving Path message with Ingress-Protection object, and sends Resv message with Ingress-Protection object to primary ingress. | 2) Primary ingress specially processes all possible abnormal cases happening in the backup ingress and in the path segment between the proxy ingress (i.e., the primary ingress), backup ingress and the primary ingress. These are changes to the existing RSVP-TE protocol, especially mixed with signaling for the primary LSP.
3) Primary ingress records the status of ingress protection after receiving Resv message with Ingress-Protection object. | 3) Primary ingress changes the path for the primary LSP. The new path for the LSP will be: the proxy-ingress (i.e., the primary ingress), the backup ingress, the primary ingress, the next hop(s) of the primary ingress, and so on.
 | 4) Primary ingress adds a new object (Ingress-Protection) into the Path and Resv messages for the primary LSP to the backup ingress.
 | 5) Primary ingress specially handles the Path and Resv messages w/ Ingress-Protection for the primary LSP from and/or to the backup ingress.
 | 6) Backup ingress specially handles the Path and Resv messages w/ Ingress-Protection for the primary LSP from and/or to the primary ingress. The procedures on the backup ingress for specially handling the Path and Resv messages are different from those on the primary ingress.
When the primary ingress fails, the backup ingress can not get any Path messages from the primary ingress (i.e., the proxy-ingress or the primary ingress), thus it must keep the Path message(s) originally received from the primary ingress, update the message(s) and put the message(s) into the bypass LSP tunnel to the next hop(s) of the primary ingress. | 
When the primary ingress fails, the backup ingress can not send any Resv message(s) to its primary ingress (i.e., its previous hop proxy-ingress or the primary ingress), thus it should keep the Resv message(s) originally received and update the message(s) such as setting Protection-in-use. | 
5

## Slide 6: Relay-Message Method with Example
6
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
2. PE6 creates backup LSP to protect PE5 through calling existing functions
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
2
3
0
Notes: 6

## Slide 7
7
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
Primary ingress PE5 :
Detects failures of backup ingress PE6, handles failures and abnormal cases in PE6 and path segments between proxy ingress and backup ingress (and between primary ingress and backup ingress), and changes the signaling path for the primary LSP when a failure or abnormal event happens in the backup ingress or the path segments.
Processes configuration for Proxy-ingress or generates the information for the proxy-ingress and makes sure that the proxy-ingress address generated does not cause a loop
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Proxy-Ingress Method with Example
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6
Notes: 7

## Slide 8: Contents
Introduction
Descriptions on Two Methods
Analysis on Two Methods
  Configurations
  Primary LSP Dependency
  Message Overhead
  Special Handlings on Primary Ingress
  Special Handlings on Backup Ingress
  Backup LSP Creation
  Primary LSP Setup Time
  Session Maintenance
  Scalability
  Summary on Analysis

## Slide 9: Configurations
Relay-Message Method:
  Configure backup ingress
Proxy-Ingress Method:
  Configure backup ingress
  Configure proxy-ingress or generate the information for the proxy-ingress and make sure that the proxy-ingress address generated does not cause a loop

## Slide 10: Primary LSP Dependency
Relay-Message Method:
Primary LSP is independent of the backup ingress. The establishment of primary LSP is not touched by adding ingress protection
Proxy-Ingress Method:
The primary LSP depends on the backup ingress somehow. The creation of primary LSP is changed for providing ingress protection. For example, the signaling messages for the primary LSP goes from the primary ingress (acting as the proxy ingress) to the backup ingress, to the primary ingress and then to the next hop(s) of the primary ingress. Thus abnormal events on backup ingress may affect the primary LSP.
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
0
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 11: Message Overhead
Relay-Message Method (2 messages):
Path Message with INGRESS_PROTECTION is sent
  from primary ingress to backup ingress
Resv Message with INGRESS_PROTECTION is sent
  from backup ingress to primary ingress
Proxy-Ingress Method (4 messages):
Path Message with INGRESS_PROTECTION is sent
  from proxy-ingress (i.e., primary ingress) to backup ingress and
  from backup ingress to primary ingress
Resv Message with INGRESS_PROTECTION is sent
  from primary ingress to backup ingress and
  from backup ingress to proxy-ingress (i.e., primary ingress)
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2
0
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 12: Special Handlings on Primary Ingress
Relay-Message Method:
sends Path with INGRESS_PROTECTION to backup ingress after primary LSP is set up
stores states after receiving Resv with INGRESS_PROTECTION from backup ingress
removes session to backup ingress when tearing down primary LSP (or failure or abnormal events in backup ingress occur)
refreshes session to backup ingress when refreshing primary LSP
Proxy-Ingress Method:
changes the ERO for primary LSP (ERO: proxy-ingress  backup ingress primary ingress  next hop  …)
sends Path with INGRESS_PROTECTION to backup ingress after changing the ERO
sends Path without INGRESS_PROTECTION to next hop after receiving Path with INGRESS_PROTECTION from backup ingress
After receiving Resv without INGRESS_PROTECTION from next hop, it does not assign a normal label for the interface from its upstream node (backup ingress), or write a cross connect from its upstream node to its next hop; it sends Resv with INGRESS_PROTECTION to its upstream node (i.e., backup ingress).
After receiving Resv with INGRESS_PROTECTION from backup ingress, stores states and write LFIB for primary LSP
detects failures of the backup ingress, handles failures and other abnormal events happening in the backup ingress and the path segments between proxy ingress and backup ingress (and between primary ingress and backup ingress), and changes the signaling path for the primary LSP when a failure or abnormal event happens in the backup ingress or the path segments.
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
0
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 13: Special Handlings on Backup Ingress
Relay-Message Method:
After receiving Path with INGRESS_PROTECTION from primary ingress, it sends Resv with INGRESS_PROTECTION to primary ingress, but does not reserve any resources
When detecting primary ingress failure, it must keep the state for the Path message(s) originally received from the primary ingress, update the message(s) and put the message(s) into the bypass LSP tunnel to the next hop(s) of the primary ingress. It keeps the state for the Resv message(s) and update the message(s) such as setting Protection-in-use.
When the state for the Path message(s) is to be removed by Path Tear from primary ingress or refresh timer expiration with primary ingress up, it tears down the backup LSP(s) through calling existing functions
Proxy-Ingress Method:
After receiving Path with INGRESS_PROTECTION from proxy-ingress, it sends Path with INGRESS_PROTECTION to primary ingress, but does not reserve any resources
After receiving Resv with INGRESS_PROTECTION from its next hop (i.e., primary ingress), it considers the case that no normal label is assigned by its next hop (i.e., primary ingress). It does not assign a normal label for the interface from its upstream node (i.e., proxy ingress or primary ingress), or write a cross connect from its upstream node to its next hop. It sends a Resv with INGRESS_PROTECTION to its upstream node (proxy-ingress), but does not reserve any resource.
When detecting primary ingress failure, it can not get any Path messages from its previous hop (i.e., the proxy-ingress or the primary ingress), thus it must keep the state for the Path message(s) originally received from the primary ingress, update the message(s) and put the message(s) into the bypass LSP tunnel to the next hop(s) of the primary ingress. It can not send any Resv message(s) to its previous hop (i.e., the proxy-ingress or the primary ingress), thus it keeps the state for the Resv message(s) originally received from its next hop (i.e., primary ingress) and update the message(s) such as setting Protection-in-use.
When the state for the Path message(s) is to be removed by Path Tear from primary ingress or refresh timer expiration with primary ingress up, it tears down the backup LSP(s) through reusing FRR with changes
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
0
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 14: Backup LSP Creation
Relay-Message Method:
Backup LSP creation through calling backup LSP creation function and LFIB entry writing function to import traffic from source into backup LSP.
Proxy-Ingress Method:
Backup LSP creation reusing FRR with changes to existing procedures. The changes include: 1) writing LFIB entry to import traffic from source into backup LSP instead of writing LFIB entry to swap incoming label to outgoing label in date packet from upstream hop (i.e., proxy-ingress or primary ingress, when primary ingress fails, traffic from source is imported to backup LSP on backup ingress); 2) getting around the procedure that sets a flag in the LFIB entry indicating inactive. The flag is used to activate the LFIB entry after failure of primary ingress is detected by backup ingress. When source detect is used, the LFIB entry for backup LSP is active always and thus setting the inactive flag needs to be prevented.
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
0
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 15: Primary LSP Setup Time
Relay-Message Method:
Primary LSP setup time after adding ingress protection is the same as before (i.e., without adding ingress protection). The setup of primary LSP is not touched after adding ingress protection.
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6
Proxy-Ingress Method:
Primary LSP setup time is longer after adding ingress protection. After adding ingress protection, the signalling of primary LSP is changed and goes through two extra hops via backup ingress (i.e., from proxy-ingress (i.e., primary ingress) to backup ingress, from backup ingress to primary ingress, and then from primary ingress to next hops of primary ingress).
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
0

## Slide 16: Session Maintenance on Primary Ingress
Relay-Message Method: (1 session)
Session (state) to backup ingress
  (refer to 1 and 3)
Proxy-Ingress Method: (2 sessions)
Session (state) to backup ingress from proxy-ingress (i.e., “primary ingress”) (refer to 1 and 6)
Session (state) from backup ingress (refer to 2 and 4)
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
1
3
2. PE6 creates backup LSP to protect PE5 through calling existing functions
2
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6

## Slide 17: Session Maintenance on Backup Ingress
Relay-Message Method: (1 session)
Session (state) from primary ingress
  (refer to 1 and 3)
Proxy-Ingress Method: (2 sessions)
Session (state) from (upstream node) proxy-ingress (i.e., “primary ingress”) (refer to 1 and 6)
Session (state) to (next hop) primary ingress (refer to 2 and 4)
LSP Path (ERO):
PE5’—PE6—PE5—NHs …
1. Proxy Ingress PE5’ (i.e., primary ingress PE5 acting as PE5’) sends Path w/ INGRESS_PROTECTION to backup ingress PE6
2. Backup ingress PE6 sends Path w/ INGRESS_PROTECTION to primary ingress PE5
PE1
PE2
PE6
PE5
PE4
PE3
PE5’
3. PE5 sends Path w/o INGRESS_PROTECTION to NHs
(NHs send Resv to primary ingress PE5)
5. PE6 creates backup LSP to protect ingress PE5 reusing FRR with changes to existing procedures
Primary LSP
Backup LSP
Path Msg
Resv Msg
4. Primary ingress PE5 sends Resv w/ INGESS_PROTECTION to backup ingress PE6 after receiving Resv from NHs
6. Backup ingress PE6 sends Resv w/ INGRESS_PROTECTION to proxy ingress PE5’ (i.e., PE5 acting as PE5’)
PE7
P1
1
2
3
4
5
6
PE1
PE2
PE6
PE5
PE4
PE3
1. Ingress PE5 sends Path w/ INGRESS_PROTECTION to backup ingress PE6 after primary LSP is set up
3. PE6 sends PE5 Resv w/ INGRESS_PROTECTION
Primary LSP
Backup LSP
Path Msg
Resv Msg
PE7
P1
2
3
1
2. PE6 creates backup LSP to protect PE5 through calling existing functions

## Slide 18: Scalability
Relay-Message Method: (2 messages, 2 session states)
2 session states
  one state for session on primary ingress (from primary ingress to backup ingress)
  one state for session on backup ingress (from primary ingress to backup ingress)
2 messages
  Path Message with INGRESS_PROTECTION is sent
    from primary ingress to backup ingress
  Resv Message with INGRESS_PROTECTION is sent
  from backup ingress to primary ingress
Proxy-Ingress Method: (4 messages, 4 session states)
4 session states
  2 session states on primary ingress (one state for session from proxy-ingress (i.e., “primary ingress”) to backup ingress; one state for session from backup ingress to primary ingress)
  2 session states on backup ingress (one state for session from proxy-ingress (i.e., “primary ingress”) to backup ingress; one state for session from backup ingress to primary ingress)
4 messages
  Path Message with INGRESS_PROTECTION is sent
    from proxy-ingress (i.e., primary ingress) to backup ingress and
    from backup ingress to primary ingress
  Resv Message with INGRESS_PROTECTION is sent
    from primary ingress to backup ingress and
    from backup ingress to proxy-ingress (i.e., primary ingress)

## Slide 19: Summary
Item \ Method | Relay-Message | Proxy-Ingress
Configurations | Less | More
Primary LSP depends on backup ingress somehow | No | Yes
Control Message Overhead | Less (2) | More (4)
Special Handlings on Primary Ingress | Less | More
Special Handlings on Backup Ingress | Less | More
Backup LSP creation and deletion | Through calling existing functions | Reusing FRR with changes to existing procedures
Primary LSP setup time after adding ingress protection | Same as before | Longer
Session State Overhead | Less (2) | More (4)
Scalability | Higher(less overheads) | Lower(more overheads)
Local Repair, Global Repair, On-Path Procedure, Revert to Primary Ingress, Backwards Compatibility, Security Considerations | Common for two methods (with minor difference for some cases) | 

## Slide 20: Thanks

## Slide 21: Local Repair on Backup Ingress
After detecting primary ingress failure, backup ingress does the followings
Relay-Message Method:
must keep the Path message(s) originally received from the primary ingress, update the message(s) and put the message(s) into the bypass LSP tunnel to the next hop(s) of the primary ingress.
keep the Resv message(s) and update the message(s) such as setting Protection-in-use.
keep session from primary ingress (inactive)
Proxy-Ingress Method:
must keep the Path message(s) originally received from the primary ingress, update the message(s) and put the message(s) into the bypass LSP tunnel to the next hop(s) of the primary ingress.
(since it can not get any Path messages from its previous hop (i.e., the proxy-ingress or the primary ingress),
keep the Resv message(s) originally received from its next hop (i.e., primary ingress) and update the message(s) such as setting Protection-in-use.
(since it can not send any Resv message(s) to its previous hop (i.e., the proxy-ingress or the primary ingress)
keep session from (upstream node) proxy-ingress (i.e., “primary ingress”) (inactive)
Let session to (next hop) primary ingress down
1, 2 and 3 are common for two methods (note 3 considered to be common)
In summary, common for two methods with minor difference

## Slide 22: Global Repair
After detecting primary ingress failure, backup ingress does the followings for global repair (common for two methods)
Relay-Message Method:
Proxy-Ingress Method:
  Compute a global optimal path
  Set up a new LSP along the path with a different LSP ID
  Switch traffic to the new LSP
  Tear down the old LSP

## Slide 23: Backwards Compatibility
Primary ingress sends Path message with INGRESS_PROTECTION to backup ingress.
If backup ingress does not support the extensions for ingress protection, then
Relay-Message Method:
  Primary ingress receives Path Err from backup ingress and sends Path Tear to backup ingress
Proxy-Ingress Method:
  Proxy-ingress (i.e., “Primary ingress”) receives Path Err from backup ingress and sends Path Tear to backup ingress
  Primary ingress changes the ERO and sends Path message with the updated ERO to its next hops after determining that backup ingress does not support ingress protection
common for two methods with minor difference

## Slide 24: Details in Existing P2MP LSP Ingress & Egress Protections
To provide E2E P2MP LSP protection，a current way (detail in next page)
  Redundant Root and Every Leaf
  Create two P2MP LSPs from root to leaves, carry the same data at same time.
  For each leaf, create a P2P LSP from the leaf to root and configure BFD with it
  Run iBGP on every leaf node and use P2P LSP as its next hop
  When BFD detects P2P LSP failure, BGP withdraws route to root and this makes the receiver switch to another leaf to get the data.

## Slide 25: Details in Existing P2MP LSP Ingress & Egress Protections (Cont)
P2MP
Multicast
Source
Multicast
Receiver
Data
PE2
PE1
PE10
PE9
CE2
CE1
CE4
CE1
Primary P2MP LSP
Backup P2MP LSP
Data
PE7
PE8
CE3
IGMP Join
PE3
PE4
PE5
PE6
1. Double leaves
2. Two P2MP LSP carry data
3. P2P LSP (leafroot) with BFD
4. P2P LSP as NH to SA, export route for SA to receiver
5. Receiver selects a leaf accordingly
P2P LSP

## Slide 26: Issues in Existing P2MP LSP Ingress & Egress Protections
Not easy to operate
  For each P2MP LSP branch/sub-LSP,
    need configure a reverse P2P LSP from leaf to root with BFD
    P2P LSP with BFD is used to detect failure of its corresponding P2MP sub-LSP
Not reliable
  The failure of reverse P2P LSP from leaf to root does not mean the failure of its corresponding P2MP sub-LSP from root to leaf
Consume lots of resource
  Reserve/use double bandwidth
Speed of Global Recovery
  Depends on convergence of IGP and BGP

## Slide 27: Advantages of P2MP LSP Ingress and Egress Local Protection
All parts of P2MP LSP are locally protected
Only one P2MP LSP is used to implement an E2E protection
  Normally two P2MP LSPs are used
Big saving on resource : 50% bandwidth saving
  No need to reserve/use double bandwidth
Faster recovery
  Speed of local protection recovery
  Flow recovery within 50ms when a failure happens
Easier to operate